## Slide 1: Tutorial: a Practical Introduction to using Event-B for Complex Hardware and Embedded System Specification and Design
John Colley
FDL 2012
Vienna

## Slide 2: Introduction
Background to Event-B
Event-B in the Design/Verification Flow
Complex hardware specification/verification
  Pipelines
  Elastic Buffering
Embedded system specification/verification
  Temporal Modeling in Cyber-physical systems
  Animating and Model Checking Event-B models
Assertion-based verification
  Deriving assertions from the specification
Summary

## Slide 3: Background to Event-B
Event-B is a formal method for system-level modelling and analysis which uses
  set theory as a modelling notation
  refinement to represent systems at different abstraction levels
  mathematical proof to verify consistency between refinement levels.
The Rodin Platform is an Eclipse-based IDE for Event-B
  provides support for refinement and mathematical proof
  open source
ProB is an animator and model checker in the Rodin environment

## Slide 4: Industrial Deployment of Event-B
Deploy (FP7 – completed 2012)
  Bosch have been working on developing a cruise control system and a start-stop system
  Siemens Transportation have been working on train control and signalling systems
  Space Systems Finland have been working on part of the BepiColombo space probe and on Attitude and Orbit Control System software(AOCS)
  SAP have been working on analysis of business choreography models
  Systerel are working on railway and aerospace systems
ADVANCE (FP7 – started Oct 2011)
  Event-B for Cyber-Physical Systems
  http://www.advance-ict.eu/

## Slide 5: Event-B in a Design /Verification Flow
Requirements/Safety Analysis
Specification Refinement
Architectural Refinement
Implementation Verification

## Slide 6: Event-B in a Design /Verification Flow
Requirements/Safety Analysis
Specification Refinement
Architectural Refinement
Implementation Verification
Event-B Refinement

## Slide 7: Event-B in a Design /Verification Flow
Requirements/Safety Analysis
Specification Refinement
Architectural Refinement
Implementation Verification
Event-B Refinement
Event-B
Code and Assertion
Generation

## Slide 8: A MicroProcessor Pipeline
Each pipeline stage is a process running concurrently with all the other stages
Communication is by shared variables (pipeline registers)
New high-level languages speed up design
  Bluespec
    Guarded atomic actions
    High-level synthesis to RTL
But verification is still
  performed on low-level RTL description
  predominantly test-based

## Slide 10: Pipeline Verification Goals
Start Verification at the Specification Level
Explore micro-architectural alternatives at the specification level
Close the gap between specification and implementation
Exploit synergy with Bluespec
Incorporate proof-based techniques into the established SoC verification flow

## Slide 11: Specifying an Arithmetic Instruction
context PIPEC
constants Register Rr Ra Rb ArithRROp
sets Op // Operations
axioms
@axm1 Register ⊆ ℕ // Processor Register Identifier
@axm2 Rr ∈ Op → Register // Destination Register
@axm3 Ra ∈ Op → Register // First Source Register
@axm4 Rb ∈ Op → Register // Second Source Register
@axm5 ArithRROp ⊆ Op // Register/Register Arithmetic Ops
end

## Slide 12: The Abstract Machine
machine PIPEM sees PIPEC
variables Regs
invariants
@inv1 Regs ∈ Register → ℤ // The Processor Register File
events
event INITIALISATION
then
@act1 Regs ≔ Register × {0}
end
event ArithRR
any pop
where
@grd1 pop ∈ ArithRROp
then
@act1 Regs(Rr(pop)) ≔ Regs(Ra(pop)) + Regs(Rb(pop))
end
end

## Slide 13: The Abstract Architecture
Regs
ArithRR
pop

## Slide 14
Regs
ArithRR
pop
event ArithRR
any pop
where
@grd1 pop ∈ ArithRROp
then
@act1 Regs(Rr(pop)) ≔ Regs(Ra(pop)) + Regs(Rb(pop))
end
The Abstract Architecture

## Slide 15: First Refinement: a two-stage pipeline
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop

## Slide 16: Pipeline Feedback and Interleaving
v2
e1i
e2j
ppop
v1
v2
e1i
e2j
ppop
v1
e2j followed by e1i (e2j;e1i) is equivalent to e1i || e2j
there is NO interleaving that represents e1i || e2j

## Slide 17
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
event EXWBnoRAW refines ArithRR
any ppop
where
@grd1 EXop ∈ ArithRROp
@grd2 ppop ∈ ArithRROp
with
@pop pop = EXop
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
@act2 EXALUoutput ≔ Regs(Ra(ppop)) + Regs(Rb(ppop))
@act3 EXop ≔ ppop
end

## Slide 18
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
event EXWBnoRAW refines ArithRR
any ppop
where
@grd1 EXop ∈ ArithRROp
@grd2 ppop ∈ ArithRROp
with
@pop pop = EXop
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
@act2 EXALUoutput ≔ Regs(Ra(ppop)) + Regs(Rb(ppop))
@act3 EXop ≔ ppop
end
event ArithRR
any pop
where
@grd1 pop ∈ ArithRROp
then
@act1 Regs(Rr(pop)) ≔ Regs(Ra(pop)) + Regs(Rb(pop))
end

## Slide 19: The Gluing Invariant
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
@inv3 EXALUoutput = Regs(Ra(EXop)) + Regs(Rb(EXop))

## Slide 20: The Gluing Invariant
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
@inv3 EXALUoutput = Regs(Ra(EXop)) + Regs(Rb(EXop))
Parallel Execution must detect the potential
Read After Write (RAW) Hazard

## Slide 21
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
event EXWBnoRAW refines ArithRR
any ppop
where
@grd1 EXop ∈ ArithRROp
@grd2 ppop ∈ ArithRROp
@grd3 Rr(EXop) ≠ Ra(ppop)
@grd4 Rr(EXop) ≠ Rb(ppop)
with
@pop pop = EXop
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
@act2 EXALUoutput ≔ Regs(Ra(ppop)) + Regs(Rb(ppop))
@act3 EXop ≔ ppop
end

## Slide 22
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
forwarding

## Slide 23
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
forwarding
event EXWBaRAW refines ArithRR
any ppop
where
@grd1 EXop ∈ ArithRROp
@grd2 ppop ∈ ArithRROp
@grd3 Rr(EXop) = Ra(ppop)
@grd4 Rr(EXop) ≠ Rb(ppop)
with
@pop pop = EXop
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
@act2 EXALUoutput ≔ EXALUoutput + Regs(Rb(ppop))
@act3 EXop ≔ ppop
end

## Slide 24
R
e
g
s
IFIDEX
WB
IFIDEX
EXWB pipeline registers
WB
ppop
E X A L U
o
u
t
EXop
forwarding
event EXWBaRAW refines ArithRR
any ppop
where
@grd1 EXop ∈ ArithRROp
@grd2 ppop ∈ ArithRROp
@grd3 Rr(EXop) = Ra(ppop)
@grd4 Rr(EXop) ≠ Rb(ppop)
with
@pop pop = EXop
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
@act2 EXALUoutput ≔ EXALUoutput + Regs(Rb(ppop))
@act3 EXop ≔ ppop
end
Event WB
where
@grd1 EXop ∈ ArithRROp
then
@act1 Regs(Rr(EXop)) ≔ EXALUoutput
end
Decompose to obtain the
WriteBack event

## Slide 25: Forwarding and Centralised Stalling
As the pipeline gets longer
  More forwarding tracks are required
    the feedback tracks get longer
  Centralised stalling to manage branching becomes more complex and difficult to verify
    the feedback tracks get longer
Synchronous Elastic Buffers provide an alternative solution
  Latency insensitive
  Distributed stalling
  First used by Intel to meet timing requirements

## Slide 26: The SELF Protocol
IDLE
RETRY
TRANSFER
valid ⋀ stop
valid ⋀ stop
valid ⋀ stop
valid ⋀ ¬stop
valid ⋀ ¬stop
valid ⋀ ¬stop
¬valid
¬valid
Value
DATA
stop
valid

## Slide 27: Connecting two Elastic Components
Value
DATA
stop
valid
Value
DATA
elastic buffer

## Slide 28: Recall Abstract Machine Micro-architecture
Regs
ArithRR
pop
event ArithRR
any pop
where
@grd1 pop ∈ ArithRROp
then
@act1 Regs(Rr(pop)) ≔ Regs(Ra(pop)) + Regs(Rb(pop))
end

## Slide 29: Refinement with Synchronous Elastic Buffers
R
e
g
s
IFIDEX
WB
IFIDEX
SEB
WB
ppop

## Slide 30: Abstract Synchronous Elastic Buffer
. . . .
i i + 1 i + k
rd wr

## Slide 31
R
e
g
s
IFIDEX
WB
IFIDEX
SEB
WB
vbuf1
obuf1
vbuf2
obuf2
valid1
valid2
vwr2
owr2
vrd2
ord2
vwr1
owr1
ord1
vrd1
ppop
Refinement with Synchronous Elastic Buffers

## Slide 32
event EXWBnoRAW refines ArithRR
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf1(ord1) ∈ ArithRROp
@grd3 obuf2(ord2) ∈ ArithRROp
@grd4 Valid1 = TRUE
@grd5 Rr(obuf1(ord1)) ≠ Ra(pppop)
@grd6 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd8 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd9 Valid2 = TRUE
with
@pop pop = obuf1(ord1)
then
@act1 Regs(Rr(obuf1(ord1))) ≔ vbuf1(vrd1)
@act2 obuf1(owr1) ≔ obuf2(ord2)
@act3 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act4 vbuf2(vwr2) ≔ Regs(Ra(pppop)) + Regs(Rb(pppop))
@act5 obuf2(owr2) ≔ pppop
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1

## Slide 33
event EXWBnoRAW refines ArithRR
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf1(ord1) ∈ ArithRROp
@grd3 obuf2(ord2) ∈ ArithRROp
@grd4 Valid1 = TRUE
@grd5 Rr(obuf1(ord1)) ≠ Ra(pppop)
@grd6 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd8 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd9 Valid2 = TRUE
with
@pop pop = obuf1(ord1)
then
@act1 Regs(Rr(obuf1(ord1))) ≔ vbuf1(vrd1)
@act2 obuf1(owr1) ≔ obuf2(ord2)
@act3 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act4 vbuf2(vwr2) ≔ Regs(Ra(pppop)) + Regs(Rb(pppop))
@act5 obuf2(owr2) ≔ pppop
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1
Gluing Invariants
Valid1 = TRUE ⇒
vbuf1(vrd1) = Regs(Ra(obuf1(ord1))) + Regs(Rb(obuf1(ord1)))
Valid2 = TRUE ⇒
vbuf2(vrd2) = Regs(Ra(obuf2(ord2))) + Regs(Rb(obuf2(ord2)))
EXALUoutput = Regs(Ra(EXop)) + Regs(Rb(EXop))

## Slide 34
event EXWBRAWa refines ArithRR
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf1(ord1) ∈ ArithRROp
@grd3 obuf2(ord2) ∈ ArithRROp
@grd4 Valid1 = TRUE
@grd5 Rr(obuf1(ord1)) = Ra(pppop)
@grd6 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd8 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd9 Valid2 = TRUE
with
@pop pop = obuf1(ord1)
then
@act1 Regs(Rr(obuf1(ord1))) ≔ vbuf1(vrd1)
@act2 obuf2(owr2) ≔ pppop
@act3 obuf1(owr1) ≔ obuf2(ord2)
@act4 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act5 Valid2 ≔ FALSE
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1

## Slide 35
event EXstallWB refines ArithRR
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf1(ord1) ∈ ArithRROp
@grd3 obuf2(ord2) ∈ ArithRROp
@grd4 Valid1 = TRUE
@grd5 Rr(obuf1(ord1)) ≠ Ra(pppop)
@grd6 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd8 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd9 Valid2 = FALSE
with
@pop pop = obuf1(ord1)
then
@act1 Regs(Rr(obuf1(ord1))) ≔ vbuf1(vrd1)
@act2 obuf1(owr1) ≔ obuf2(ord2)
@act3 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act4 vbuf2(vwr2) ≔ Regs(Ra(pppop)) + Regs(Rb(pppop))
@act5 obuf2(owr2) ≔ pppop
@act6 Valid1 ≔ FALSE
@act7 Valid2 ≔ TRUE
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1

## Slide 36
event EXWBstall
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf2(ord2) ∈ ArithRROp
@grd2 obuf2(ord2) = obuf1(ord1)
@grd3 Valid1 = FALSE
@grd4 Rr(obuf1(ord1)) ≠ Ra(pppop)
@grd5 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd6 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd8 Valid2 = TRUE
then
@act1 vbuf2(vwr2) ≔ Regs(Ra(pppop)) + Regs(Rb(pppop))
@act2 obuf2(owr2) ≔ pppop
@act3 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act4 obuf1(owr1) ≔ obuf2(ord2)
@act5 Valid1 ≔ TRUE
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1

## Slide 37
event EXWBstall
any pppop
where
@grd1 pppop ∈ ArithRROp
@grd2 obuf2(ord2) ∈ ArithRROp
@grd2 obuf2(ord2) = obuf1(ord1)
@grd3 Valid1 = FALSE
@grd4 Rr(obuf1(ord1)) ≠ Ra(pppop)
@grd5 Rr(obuf1(ord1)) ≠ Rb(pppop)
@grd6 Rr(obuf2(ord2)) ≠ Ra(pppop)
@grd7 Rr(obuf2(ord2)) ≠ Rb(pppop)
@grd8 Valid2 = TRUE
then
@act1 vbuf2(vwr2) ≔ Regs(Ra(pppop)) + Regs(Rb(pppop))
@act2 obuf2(owr2) ≔ pppop
@act3 vbuf1(vwr1) ≔ vbuf2(vrd2)
@act4 obuf1(owr1) ≔ obuf2(ord2)
@act5 Valid1 ≔ TRUE
… // update buffer indices
end
regs
IFIDEX
WB
IFIDEX
SEB
WB
ppop
buf2
buf1
Responsiveness
Valid1 = TRUE ∨ Valid2 = TRUE

## Slide 38: Shared Event Pipeline Decomposition
R
e
g
s
IFIDEX
WB
IFIDEX
SEB
WB
vbuf1
obuf1
vbuf2
obuf2
valid1
valid2
vwr2
owr2
vrd2
ord2
vwr1
owr1
ord1
vrd1
ppop
MACHINE 1
MACHINE 2
MACHINE 3

## Slide 39: Second Refinement: MACHINE 1
R
e
g
s
IFIDEX
WB
IFIDEX
SEB
WB
vbuf1
obuf1
vbuf2
obuf2
valid1
valid2
vwr2
owr2
vrd2
ord2
vwr1
owr1
ord1
vrd1
ppop
valid
stop
MACHINE 1
MACHINE 2
MACHINE 3

## Slide 40: Pipelining Summary
Micro-architectural exploration is raised to the Specification Level using Event-B
An alternative to forwarding and centralised stalling has been explored using Synchronous Elastic Buffers
Latency Insensitivity is introduced at Low Cost
Track lengths are reduced
Synchronous Elastic Buffers allow performance goals to be met in a verifiable way
Verification is raised to the Specification Level

## Slide 41: Temporal Modeling in Cyber-physical systems
Simulating Formal Models
Modeling Timing Cycles
  Component Modes
  Generalised Update/Evaluation Modes
A Simple Example
Summary

## Slide 42: Temporal Modeling in Cyber-physical Systems: Requirements
Distributed Function and Control
Managing Safety Hazards
Verifying the relationships between Inputs and Outputs

## Slide 43: Distributed Function and Control
Controller
1
Controller
2
B
D
C1
C2
C3

## Slide 44: Distributed Function and Control
Controller
1
Controller
2
B
D
C1
C2
C3
Must Model the Communication and Synchronisation
of the Concurrent Processes

## Slide 45: Managing Safety Hazards
Plant model Evaluates
Potential Hazards are Detected
The Controller manages the Hazards
The Controller predicts the future behaviour of the Plant
Loop must be generalised for multiple controllers and distributed Plant

## Slide 46: Verifying the relationships between Inputs and Outputs
DO-178C Formal Supplement
  Must show that
    Outputs fully satisfy Inputs
    Each Output data item is necessary to satisfy some Input data item (No unintended behaviour)
  Must show that
    Input/Output specification is preserved by chosen implementation architecture
ACSL
  Ansi ISO C Specification Language
  Code annotations – used by Airbus

## Slide 47: Simulating Formal Models
Abstract Model(s) may be untimed
Refined Models represent Concurrent, Communicating Processes
  will need to introduce some notion of a tick
    Cycle-based execution
    Timed execution of Delays and Deadlines
ProB has the notion of the next state
  an event is executed (LTL X)
We need the notion of the next tick

## Slide 48: Modeling Timing Cycles: Component Modes
Eg for Hazard Analysis
  Plant Mode
  Detect Mode
  Controller Mode
  Predict Mode
Necessary to define an ordering on the modes
The Plant may need to evaluate at a much higher rate than the Controller

## Slide 49: Modeling Timing Cycles: Update/Evaluate Modes
Used by many Commercial Discrete Event Simulators
  SystemC
  Verilog/VHDL
Supports arbitrary topology complexity
No zero-delay communication between components
  Components can evaluate in any order
Components “suspend” between wake-ups
  Input change
  Self wake
  Components can evaluate at different rates
Discrete Time, Cycle-based or both

## Slide 50: Discrete Event Simulation
A
C
B
D
C1
C2
COMPONENT VIEW
Components: A, B, C, D (processes)
Connections: C1, C2 (unidirectional)
Ports: IN OUT
SIMULATOR API
GetValue(port)
HasChanged(port)
SetValue(OUT port, val, delay)
ScheduleEval(component, delay)

## Slide 51: The Two-list Simulation Algorithm
A
C
B
D
C1
C2
update
list
evaluation
list
t = 0
t = n

## Slide 52: Simulating Models without Discrete Delays – Unit Delay
A
C
B
D
C1
C2
update
list
evaluation
list
Each evaluate/update
cycle advances time by
one tick

## Slide 53: A Simple Arithmetic Example The Abstract Specification – Output as a function of Inputs
event AddInc
any p
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
then
@act1 v ≔ In1(p) + In2(p) + 1
end
constants Inputs In1 In2
sets Parameters
axioms
@axm1 Inputs ⊆ Parameters
@axm2 In1 ∈ Inputs → ℕ
@axm3 In2 ∈ Inputs → ℕ
end

## Slide 54: The Implementation Architecture
event AddInc
any p
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
then
@act1 v ≔ In1(p) + In2(p) + 1
end
⊆
Add
Increment
Channel: sum
Delay = 2

## Slide 55: The Implementation Architecture
event AddInc
any p
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
then
@act1 v ≔ In1(p) + In2(p) + 1
end
⊆
Add
Increment
Channel: sum
Delay = 2
Does the chosen Architecture Implement the Abstract Specification?
Output as a function of Inputs
(DO-178C)

## Slide 56: Modelling Channels with Delay in Event-B
A Channel is a Set of Schedules
A Schedule comprises
  a Delay (greater than or equal to 0)
  a Value (optional)
  the Input Values that correspond to the Output Value (optional)
Delay
Value
Inputs
Delay
Value
Inputs
Delay
Value
Inputs
,
,

## Slide 57: Writing to a Channel
A Channel write is accomplished by creating a new schedule with a delay of at least one
Multiple Schedules may be added
  Prevent multiple schedules for same time OR
  Choose one non-deterministically
2
Value
Inputs
1
Value
Inputs
6
Value
Inputs
,
,

## Slide 58: The Update/Evaluate Cycle
Update is modeled using a single Event-B event
Evaluate is represented by one or more enabled Component Events
2
Value
Inputs
1
Value
Inputs
6
Value
Inputs
,
,

## Slide 59: Evaluation Mode
All Components, where one or more of their Input Channels has a schedule with delay 0, resume (at least one Component event is enabled and the Update event is disabled)
  Change local state
  Create new Schedules on Output Channels
  Suspend
1
Value
Inputs
0
Value
Inputs
5
Value
Inputs
,
,

## Slide 60: Update Mode
The Update Event is enabled when all the Components have been evaluated
  Schedules with 0 delay are deleted
  All other schedule delays are decremented
  The current tick is therefore complete
The Update Event is re-enabled if no schedule has 0 delay, resulting in another tick
0
Value
Inputs
0
Value
Inputs
4
Value
Inputs
,
,

## Slide 61: Our Example: The First Refinement
@inv3 sum_value ∈ Schedule ⇸ ℕ
@inv4 sum_delay ∈ Schedule ⇸ ℕ
@inv5 sum_inputs ∈ Schedule ⇸ Inputs
Add
Increment
Channel: sum
Delay = 2
Modelling the Channel

## Slide 62: The Add and Increment Components
event Add
any p s
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
@grd4 s ∉ dom(sum_delay)
@grd5 adder_evaluated = FALSE
then
@act1 sum_value(s) ≔ In1(p) + In2(p)
@act2 sum_delay(s) ≔ 2
@act3 sum_inputs(s) ≔ p
@act4 adder_evaluated ≔ TRUE
end
event Increment refines AddInc
any s
where
@grd1 s ∈ dom(sum_delay)
@grd2 sum_delay(s) = 0
@grd3 incrementer_evaluated = FALSE
with
@p p = sum_inputs(s)
then
@act1 v ≔ sum_value(s) + 1
@act2 inc_sum ≔ sum_value(s)
@act3 incrementer_evaluated ≔ TRUE
end
@inv3 sum_value ∈ Schedule ⇸ ℕ
@inv4 sum_delay ∈ Schedule ⇸ ℕ
@inv5 sum_inputs ∈ Schedule ⇸ Inputs

## Slide 63: The Update Event/Synchronisation
event Update
where
@grd1 adder_evaluated = TRUE
@grd2 0 ∉ ran(sum_delay) ∨ incrementer_evaluated = TRUE
then
@act1 adder_evaluated ≔ FALSE
@act2 incrementer_evaluated ≔ FALSE
@act3 sum_delay ≔ λi·i ∈ dom(sum_delay) ∧ sum_delay(i) > 0 ∣ sum_delay(i) − 1
@act4 sum_value ≔ λi·i ∈ dom(sum_value) ∧ i ∈ dom(sum_delay) ∧ sum_delay(i) > 0 ∣ sum_value(i)
@act5 sum_inputs ≔ λi·i ∈ dom(sum_inputs) ∧ i ∈ dom(sum_delay) ∧ sum_delay(i) > 0 ∣ sum_inputs(i)
end
event Add
any p s
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
@grd4 s ∉ dom(sum_delay)
@grd5 adder_evaluated = FALSE
then
@act1 sum_value(s) ≔ In1(p) + In2(p)
@act2 sum_delay(s) ≔ 2
@act3 sum_inputs(s) ≔ p
@act4 adder_evaluated ≔ TRUE
end
event Increment refines AddInc
any s
where
@grd1 s ∈ dom(sum_delay)
@grd2 sum_delay(s) = 0
@grd3 incrementer_evaluated = FALSE
with
@p p = sum_inputs(s)
then
@act1 v ≔ sum_value(s) + 1
@act2 inc_sum ≔ sum_value(s)
@act3 incrementer_evaluated ≔ TRUE
end

## Slide 64: The Gluing Invariant
@inv9 ∀s·s ∈ dom(sum_value) ⇒ sum_value(s) = In1(sum_inputs(s)) + In2(sum_inputs(s))
Represented as the function of Inputs to Output
as preserved in the Schedules

## Slide 65: The Second Refinement – Remove Inputs
65
event Update
where
@grd1 adder_evaluated = TRUE
@grd2 0 ∉ ran(sum_delay) ∨ incrementer_evaluated = TRUE
then
@act1 adder_evaluated ≔ FALSE
@act2 incrementer_evaluated ≔ FALSE
@act3 sum_delay ≔ λi·i ∈ dom(sum_delay) ∧ sum_delay(i) > 0 ∣ sum_delay(i) − 1
@act4 sum_value ≔ λi·i ∈ dom(sum_value) ∧ i ∈ dom(sum_delay) ∧ sum_delay(i) > 0 ∣ sum_value(i)
end
event Add
any p s
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
@grd4 s ∉ dom(sum_delay)
@grd5 adder_evaluated = FALSE
then
@act1 sum_value(s) ≔ In1(p) + In2(p)
@act2 sum_delay(s) ≔ 2
@act4 adder_evaluated ≔ TRUE
end
event Increment refines AddInc
any s
where
@grd1 s ∈ dom(sum_delay)
@grd2 sum_delay(s) = 0
@grd3 incrementer_evaluated = FALSE
then
@act1 v ≔ sum_value(s) + 1
@act2 inc_sum ≔ sum_value(s)
@act3 incrementer_evaluated ≔ TRUE
end

## Slide 66: Cycle-Based Simulation- Represent Schedules as Pairs of Variables
66
event Update refines Update
where
@grd1 adder_evaluated = TRUE
@grd2 msg_rcvd_on_sum = FALSE ∨ incrementer_evaluated = TRUE
then
@act1 msg_rcvd_on_sum ≔ msg_sent_on_sum
@act2 sum ≔ sum_prime
@act3 msg_sent_on_sum ≔ FALSE
@act4 adder_evaluated ≔ FALSE
@act5 incrementer_evaluated ≔ FALSE
end
event Add refines Add
any p
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
@grd4 adder_evaluated = FALSE
then
@act1 sum_prime ≔ In1(p) + In2(p)
@act2 msg_sent_on_sum ≔ TRUE
@act3 adder_evaluated ≔ TRUE
end
event Increment refines Increment
where
@grd1 msg_rcvd_on_sum = TRUE
@grd2 incrementer_evaluated = FALSE
then
@act1 v ≔ sum + 1
@act2 incrementer_evaluated ≔ TRUE
end

## Slide 67: Cycle-Based Simulation- A Pair of Gluing Invariants
67
@inv9 msg_rcvd_on_sum = TRUE ⇒ sum = In1(sum_inputs) + In2(sum_inputs)
@inv10 msg_sent_on_sum = TRUE ⇒ sum_prime = In1(sum_inputs_prime) + In2(sum_inputs_prime)

## Slide 68: Animating and Model Checking Event-B models with ProB
68
DEMONSTRATION

## Slide 69: Architectural Refinement
Output
Port
Input
Port
Par.
Inputs
Channel
With Delay
Par.
Inputs
⊆
v
v
AddInc
o_sum
i_sum
Add
Increment
SendResult(value, delay)
ReceiveResult(value)
event AddInc
any p
where
@grd1 p ∈ Inputs
@grd2 In1(p) ∈ ℕ
@grd3 In2(p) ∈ ℕ
then
@act1 v ≔ In1(p) + In2(p) + 1
end

## Slide 70: Cyber-physical Modeling Summary
Update/Evaluate Simulation semantics can be formalised in Event-B
Event-B component models can be simulated/co-simulated with third party simulators
Event-B refinement supports naturally the DO-178C requirement to verify the relationship between Inputs and Outputs at Specification and Implementation Level
Update/Evaluate modes provides a suitable basis for a Formal Safety Analysis
70

## Slide 71: Assertion-based Verification
Identify Assertions at the Specification Level
  Event-B Invariants
    Abstract Level
    Concrete Level
Translate Invariants to
  PSL
  SVA
Translate Synthesised Assertions to Event-B
  Formal Proof
  Model Checking
Assertion Coverage
  Trace back to Requirements

## Slide 72: Summary
Background to Event-B
Event-B in the Design/Verification Flow
Complex hardware specification/verification
  Pipelines
  Elastic Buffering
Embedded system specification/verification
  Temporal Modeling in Cyber-physical systems
  Animating and Model Checking Event-B models
Assertion-based verification
  Deriving assertions from the specification