## Slide 1: Coastal City and Ocean Renewable Energy: Pathway to an Eco San Andres
Presented by Green Team
Picture source: http://www.scafo.com.br/sp/san-andres/

## Slide 2: A Tale of Coastal Eco Cities

## Slide 3: A Tale of Coastal Eco Cities
Our Definition:
Waste/Pollution
Other Externalities
Economic Activity
Financial Service
Recreation & Leisure
Health
Education
Housing
Infrastructure
Industry
Urban Environment
Transportation
Innovations
Energy, Food, Water
Energy
Food
Water
Coastal Environment
Biotic environment:
Abiotic environment:
Species
Currents, tides, waves, wind, seafloor, water quality, mineral resources…
Land-sea interface
Waste/Pollution
Fishing
Aquaculture
Minerals
Non-renewable
energy
Renewable energy

## Slide 4: A Tale of Coastal Eco Cities
Our Definition:
Economic Activity
Financial Service
Recreation & Leisure
Health
Education
Housing
Infrastructure
Industry
Urban Environment
Transportation
Innovations
Energy, Food, Water
Energy
Food
Water
Waste/Pollution
Other Externalities
Coastal Environment
Biotic environment:
Abiotic environment:
Species
Currents, tides, waves, wind, seafloor, water quality, mineral resources…
Land-sea interface
Waste/Pollution
Fishing
Aquaculture
Minerals
Non-renewable
energy
Renewable energy

## Slide 5: A Tale of Coastal Eco Cities
Genoa, Italy
Hong Kong, China
Lagos, Nigeria
New York, US
San Andres, Colombia
Ocean Renewable Energy

## Slide 6: A Tale of Coastal Eco Cities
Eco San Andres
Legal Requirements
Financial Plan &Marketing Scheme
Ocean Renewable Energy
Government-Centred Scenario
Community-oriented Scenario
Transferability
System Scope:

## Slide 7: San Andres (Isla de San Andrés)
An island is located in the Colombian Basin of the western Caribbean Sea
Population: 70,000
Area:
Capital city of the Archipelago of San Andres, Old Providence and Santa Catalina;
UNESCO Biosphere Reserve
Main economic activity: tourism;
2010 GDP :
Basics
Caribbean Sea

## Slide 8: San Andres (Isla de San Andrés)
Natural Environment
Bathymetric features near San Andres (British Oceanographic Data Centre, 2010)
The Caribbean Sea has a variable bottom topography and remarkably irregular coastlines which affect significantly the physical processes at work in the region.
The island has an elongated shape of about long and wide.
The eastern side of the island has relatively shallow water depths and gentle slopes descending to within about from the coast.
On the eastern side the island is flanked by a coral reef barrier.
The western side has steeper slopes and reaches depths of over in less than from the coast.

## Slide 9
San Andres (Isla de San Andrés)
Challenges
    Mono Economy;
    Dependency on external supplies (food and oil) shipped from the mainland;
    Scarcity of drinkable water resources;
    Land and water pollution.
Energy demand of the island is about which is generated from a power station that runs on diesel oil.
Annual diesel consumption:
Annual emissions of CO2 to the atmosphere: ().
Energy Profile

## Slide 10
OTEC is used to extract energy from the ocean by using the temperature difference between warm surface waters and cold deep waters (ΔT ≥ 20°C).
Unlimited resource in inter-tropical regions.
Steady supply (24/7) all year round.
A sustainable energy supply system for San Andres:
Ocean Thermal Energy Conversion (OTEC)
Technology at early stage of commercialization
High capital cost Need for strong involvement of the central government.
ΔT~20°C
ΔT~23°C
Climatological monthly mean temperature averaged over the western Caribbean Sea. Adapted from Sheng and Tang (2003).
1000 m
1000 m
Government-Centred Scenario(OTEC)

## Slide 11
Working fluid: Ammonia
Products: Electricity
cold seawater
Working fluid: Sea water
Products: Electricity
cold seawater
desalinated water
CC(Closed Cycle)
OC(Open Cycle)
technology recommended for San Andres: OTEC Open Cycle
Closed Cycle (CC) vs Open Cycle (OC) OTEC technologies

## Slide 12
A 10 MW OTEC system for San Andres
Fresh water produced by OTEC | 13 million m3/year
Potable water demand in San Andres | 10 million m3/year
Current potable water supply | 5 million m3/year
Part of excess potable water will be commercialized as bottled water.
Levelized cost of electricity (capital cost, O&M,R&R): 0.36 $/kWh
Assuming a 20 years loan, interest of 4%, and inflation of 3%.
Can only be viable if both ELECTRICITY and FRESH WATER are priced

## Slide 13
OTEC Levelized Cost of Electricity
(LCOE)
Price of domestic Water
(PDW)
Price of electricity
(POE)
Profit of Bottled Water
(PBW)
Price of water
(POW)
0.36 $/kWh
Breakdown of the levelized cost of electricity (LCOE)

## Slide 14
PDW ($/m3)
PBW ($/m3)
POE ($/Kwh)
current cost of domestic water
Current cost of electricity
Profit zone
(negative PDW)
Breakdown of the levelized cost of electricity (LCOE)
POE: Price of Electricity
PDW: Price of Domestic Water
PBW: Price of Bottled Water
QE: 0.16 m3/kWh
Q: 12 million m3/year
qd: 10 million m3/year
qb: 0.15 million m3/year

## Slide 15
 | Current Cost | OTEC scenario | Relative change
Price of Electricity (POE) | 0.16 $/kWh | 0.13 $/kWh | cheaper
Price of domestic water (PDW) | 1.2 $/m3 | 0.8 $/m3 | cheaper
 | Contribution to LCOE
Price of Electricity (POE) | 0.13 $/kWh
Price of domestic water (PDW) | 0.10 $/kWh
Price of bottled water (PBW) | 0.13 $/kWh
Levelized Cost of Electricity (LCOE) : 0.36 $/kWh
Results of cost analysis of OTEC system for San Andres
Government-Centred Scenario(OTEC)
Breakdown of Levelized Cost of Electricity

## Slide 16: Alternative?
Government-centered (OTEC)
??
A renewable San Andres
Community oriented approach
Public engagement
Relative low investment
Proven technology
Community-Oriented Scenario
Community-oriented approach

## Slide 17
Community involvement
Economic activities
Samsø case since 1997 - 100% renewable energy Island in 10 years
Source : PRO AKIS, http://www.proakis.eu/
Environmental
awareness
Community-Oriented Scenario

## Slide 18
Offshore wind – development trend
Source: EWEA. (2009). Oceans of Opportunity - Harnessing Europe’s largest domestic energy resource
Community-Oriented Scenario

## Slide 19
Offshore wind – cost
Source: EWEA. (2009). The Economics of Wind Energy. “Costs of generated power comparing conventional plants to wind power, year 2010”
Source: IEA. (2008). World Energy Outlook. “Electricity generating costs in selected regions”
Community-Oriented Scenario

## Slide 20
System configuration | 
Total power output | 10MW wind farm with fixed foundation
Location | North or North East of San Andres
Integration | To be connected to transmission grid with the existing diesels plant to balance daily consumption
Community-Oriented Scenario
Financial planning | 
20% of the investment cost to be funded by local citizens | Million $2.7
Individual shares (investment cost) for each local citizen | $2,700
Levelized Cost of Energy | 0.13 kWh

## Slide 21: Legal Review for San Andres
The ocean boundaries (UN, 1982)
International Legislation
Exclusive economic zone (EEZ)
- the UNCLOS (Part V)
A zone beyond and adjacent to the territorial sea in which a coastal state has sovereign rights;
Outer limit of the EEZ shall not exceed 200 nautical miles from the baselines
Layout of submarine cables and pipelines (article 79
Colombian Rules
National Policy of Ocean and Coastal Areas with operative branches at national, regional and local level:
Goal: carry out an integrated strategy in energy sector that includes renewables
Different tributary oriented rules to incentivize investment in renewables

## Slide 22: Marketing Scheme
Possible accommodations for eco-tourism (Source: Costa Rica Star, Colombia travel, homeaway.com, sumtravel.com)
Eco San Andres needs an adequate tourism marketing campaign that introduces the island to new target market: the eco tourists.
Optimal use of environmental resources
Respect the socio-cultural authenticity of host communities
Long term sustainability.
Goal: achieving satisfaction of local inhabitants and respecting the environment while maintaining a high level of tourist satisfaction

## Slide 23: Transferability
OTEC plant must be located in a tropical zone;
OTEC solution is feasible for coastal cities or islands;
Appropriate depth to reach cold deep water should be reached within short distance from the coast;
OTEC solution can be a solution for cities with a need of water supply;
Availability of funding options and/or political to support the substantial cost of the project.
  Transferability of the OTEC proposal
  Transferability of the community oriented approach
Involvement of local stakeholders at all levels (residents, shop owners, hotel managers, politicians, etc.) throughout entire life cycle;
The identification of the right community to carry out the pilot project is vital;
Building awareness of the importance of changing energy

## Slide 24: Conclusions
A portfolio of solutions (different scale, cost, production level) is a suitable approach for energy production in coastal cities.
Under both scenarios the cost of energy (water) for final users will be lower than the current one.
Consistent investments are required and should be driven by a strong political commitment.
Both scenarios will reduce the level of emissions and GHG while generating positive effects on energy consumption patterns, water supply, possible hydrogen production for clean transportation and create consensus and awareness.
Positive spill overs to other sectors towards greener solutions can be generated.