Meta-Data Report for Windermere Bathymetry

Data was collected by the British Geological Survey in September 2010 in association with the University of Southampton in both the north and south basins of Windermere in the English Lake District. Data was analysed by Helen Miller and Jonathan Bull from the University of Southampton as well as Carol Cotterill from the British Geological Survey. The data is freely available for download and it would be appropriate to cite the following reference when using the data:

Miller, Helen, Bull, Jonathan M., Cotterill, Carol J., Dix, Justin K., Winfield, Ian J., Kemp, Alan E.S. and Pearce, Richard B. (2013) Lake bed geomorphology and sedimentary processes in glacial lake Windermere, UK. Journal of Maps, 9, (2), 299-312. (doi:10.1080/17445647.2013.780986).

The data is not appropriate for navigational use.

Further information on the survey is available at:

http://www.bgs.ac.uk/research/highlights/2013/lakeWindermere.html

A pdf map of the multibeam data is available in Eprints, and the data can be downloaded here at 1 m and 5 m resolutions from the north and south basins of Windermere.

| Survey Start Date | 17-09-10 |
| --- | --- |
| Survey End Date | 27-09-10 |
| Primary Bathymetric Instrument Type | (SIMRAD Kongsberg 300 kHz EM3002D dual head system) |
| Primary Navigation Type | DGPS |
| Horizontal Datum |  |
| Coordinate type |  |
| Projection (if applicable) | 30N |
| Vertical Datum |  |
| Reduction of Sounding to Datum Method | Data set back to a Chart Datum, which is the local datum set by the Environment Agency. This is 39.006 m above OD Newlyn |
| Intellectual Property Rights, Principal Ownership | British Geological Survey |
| Do you agree to the data being made available to the public via the UKHO INSPIRE portal? (Please note that unless otherwise specified, the data will be made available) | YES |

| Survey Name | BGS_2010_9_Windermere |
| --- | --- |
| Hydrographic Instruction (HI) Number (if applicable) | n/a |
| Block Number/Designation (if applicable) | n/a |
| Area Surveyed (give polygon coordinates in WGS84 Lat & Long, or supply text file) | Windermere within polygon, bounding coordinates: 501452, 6030113; 505046, 6030113; 501452, 6014676; 505046, 6014676 |
| Country Location of Data | UK |
| Classification / Protective Marking |  |
| Survey Company / Collecting Organisation | British Geological Survey |
| Collection Organisation Country | UK |
| Principle Purpose for Collection Of Data |  |
| Name Of Main Survey Vessel | R/V White Ribbon |
| Contact For Survey Queries | Rhys Cooper (British Geological Survey); rcooper@bgs.ac.uk |

Data details

| Survey Standard |  |
| --- | --- |
| Survey Category / IHO Order Achieved |  |
| Number of Raw Data Files/ Folders Delivered | 4 (North Basin 1 m, South Basin 1 m, North Basin 5 m, South Basin 5 m) |
| Number of Processed Survey Lines Delivered | n/a |
| Processing Software and Version Used | CARIS HIPS/SIPS Version 7 |
| Unresolved Problems or Other Notable Data Issues | NO |
| Wreck Data to Follow in Full RoS / H525? |  |
| Further Comments: | n/a |

Other information

| Calculated Scale of Survey (if applicable) | n/a |
| --- | --- |
| IPR Principal Ownership Country | UK |
| Commissioning Organisation | British Geolgical Survey |
| Commissioning Organisation Country | UK |