(

AI-HM Based Zero Portion Effects and Phase-Shift Optimization for Railway Auxiliary Inverter with Pulsating DC-Link

Lijun Diao, Member, IEEE, Lei Wang, Member, IEEE, Huiqing Du, Lu Wang, Member, IEEE, Zhigang Liu, and Suleiman M. Sharkh, Senior Member, IEEE

Abstract—High frequency pulsating DC-link inverter (PDCLI) has higher power density than conventional fixed DC-link inverter (FDCLI), and more complicate modulation methods owing to the coupling between the front-end and the last stage links. This paper analyzes the zero portion effects on the output voltage of railway auxiliary inverter with pulsating DC-link based on approximately independent hybrid modulation technique, and proposes a carrier phase-shift optimization strategy. Average mathematical models of output voltage are built, and Fourier series of the voltage difference is derived for further analysis. The output voltage performances under different conditions are compared in time-domain simulation. The results of simulation and experiments show that the proposed phase-shift approach reduces the zero portion effects and performs as well as that of FDCLI.

Index Terms—Pulsating dc-link, railway auxiliary inverter, zero portion, approximately independent hybrid modulation, phase-shift.

# INTRODUCTION

D

C-AC converters with isolation transformers are widely applied in on-board auxiliary inverters for rail vehicles, where high power density and long life cycle are required [1]-[5]. With the development of semiconductor devices and magnetic materials, the topology based on high-frequency isolation is gradually replacing that using line-frequency isolation. It reduces the weight and volume of energy-storing components, hence the power density of the system increases. In conventional fixed DC-link inverter (FDCLI), the voltage across DC-link is often obtained by a low-pass filter, which is connected after the DC-DC converter and consists of high-frequency inductors and large-capacity capacitors. In order to improve the power density to a higher level, a new topology called pulsating DC-link inverter (PDCLI) is proposed in [6] and [7].

A typical topology of PDCLI applied in railway auxiliary inverters is shown in Fig.1, which includes a high-frequency DC-DC converter which uses a high-frequency transformer for isolation, a three-phase voltage source inverter (3-VSI) and a three phase low-pass filter (LPF). The LPF after the DC-DC converter is removed, which reduces the order of the system [8], and implies that the operational life span and reliability of PDCLI are no longer affected by the inductor and capacitor of LPF [9]-[11]. But the leakage inductance of isolated transformers could cause voltage spikes on the secondary side semiconductors, snubbers must be used to overcome it [2]. The topology of PDCLI ensures higher efficiency, less weight and more modularity of the isolated DC-AC.

Fig. 1. The topology of general PDCLI

Without LPF, the DC-Link voltage after DC-DC conversion has high-frequency pulses. Due to the coupling between the front-end and last stage switching network (i.e. between the DC-DC converter and the 3-VSI), it is not applicable in this case to use the conventional scheme where all the switching networks operate regardless of the external coupling relationships. Then an approximately independent hybrid modulation (AI-HM) scheme is proposed in [12], where the front-end DC-DC converter works under quasi-180° square modulation scheme, and the 3-VSI uses conventional sinusoidal PWM (SPWM) scheme (as explained in [13]). Further more, to improve the system performance, M. Sharifzadeh et al. proposed a SHM-SHE-pulse-amplitude modulation strategy to demonstrate a significant improvement in the harmonic content of output voltage waveform [14], [15]; soft-switching condition in [16] is provided to increase the efficiency and performance of the converter without using any auxiliary circuits; and the authors of [17] and [8] used interesting two-reference dual three-pulse modulation (DTPM) for front-end converter and 33% modulation for next stage six-pack inverter to produce three-phase output and improve the efficiency, but the overall inverter has to be considered as a single unit and the two stages function in synchronism, and additional commutation semi-conductors instead of diodes are needed for pulsating dc link.

On the other hand, dead time is necessary in DC-DC triggering signals to avoid leg shoot through, or the duty cycle of DC-DC switching devices can be varied to regulate DC output voltage, both devices in the same leg will be shut off and the output voltage after rectifying is zero. Define the zone with zero output voltage to be zero portion (ZP). For PDCLI modulated by AI-HM, the existence of ZP would finally affect output voltage of 3-VSI in terms of harmonics, DC voltage utilization and DC bias [12], [18]. The increase of ZP width will deteriorate these problems. The offset and voltage distortion of 3-VSI output are discussed in [19], which are caused by zero voltage recess in DC-Link. However, this approach is not applicable in the case of PDCLI due to its inherent coupling between ZP distribution and 3-VSI modulation scheme. The authors of [20] analyzed the commutation of PDCLI the harmonic distortion of 3-VSI output and how the distortion can be compensated. The compensation is based on saw tooth carrier modulation, which can be readily realized digitally but results in high harmonics. Meanwhile, it did not consider the improvement of other properties. To solve this problem, [20] proposed a subsection compensation strategy of modulated wave, which alleviates the effect of ZP in a wide range of modulation index. Although the strategy shows obvious improvements, there is an upper limit of the compensation signal. When the amplitude of superimposed compensation signal on the modulated wave exceeds this limit, the output voltage quality of 3-VSI is affected by the existence of non-linear modulation or over modulation.

To develop a suitable optimization strategy for PDCLI modulated by AI-HM, this paper proposes a carrier phase-shift optimization strategy and is organized as follows. Section II analyzes the impacts of ZP on 3-VSI output, then carrier phase shift optimization strategy is developed. And an average mathematical model of 3-VSI output is built, together with the Fourier analysis of the voltage difference. In Section III the main characteristics of the output voltage under different ZPs are compared in time-domain simulations. The results of simulations and experiments are presented and discussed in Section IV. Conclusions are given in Section V.

# Analysis and optimization of Zero Portion Effects

## Analysis of ZP effects based on AI-HM

Define P as a frequency difference factor between uc1 and uc2, where uc1 and uc2 is the triangle carrier used in the modulation of DC-DC converter and 3-VSI, respectively:

(1)

where fo is the fundamental frequency of 3-phase output voltage. Nc1, Nc2 are the carrier frequency ratios and fc1, fc2 are the carrier frequencies of DC-DC converter and 3-VSI, respectively.

Fig.2 shows the modulation waveforms of the DC-DC converter and the 3-VSI under different values of P. The case of P=1 with SPWM modulated 3-VSI is taken as an example. In linear modulation region, ua, ub and uc, which are the voltages between output terminals of 3-VSI and the neutral point of DC-Link (i.e. the phase voltage), change between positive and negative DC bus voltage along with u*a, u*b and u*c, which are the modulation waves of the three phases of 3-VSI. Meanwhile, the phase-to-phase voltages uab, ubc and uca change between DC-Link voltage and zero. It should be noted that DC-Link voltage is the difference between positive and negative DC bus voltages.

The region with zero line voltage of 3-VSI is defined to be ideal portion (IP), where the corresponding phase voltages are the same. The other regions are the effective portions (EP). It is obvious that IPs are distributed symmetrically around vertexes of triangle carrier. IPs are decided by the pulsating voltages (the narrowest pulses), such as IP1 and IP2 in Fig.2. The phase-to-phase output voltages are not affected when ZP of DC-Link voltages are located in EPs.

Fig. 2. Mechanism of zero portions

Ideal portion does not exist in the phase output voltage of 3-VSI, because of its inherent two-level nature. Therefore, ZP of DC-Link voltage would surely affect phase output voltage of 3-VSI, as is shown in the shadow areas of ua, ub and uc in Fig.2. As for the line output voltages, by choosing a proper P value and thus relocating the ZPs in IPs, the effect of ZP can be eliminated. As is shown in Fig.2, with P = 2, there are four ZPs in each carrier period, and the number of IP is not enough. When P is a reciprocal of an integer, i.e., fc2 is integral multiple of fc1, all ZPs would fall into IPs.

However, the phase voltage quality is essential for a system with single-phase load, and phase harmonics are also key in the design of output filter. Therefore, this paper focuses on the phase voltage instead of the line voltage. In order to reduce the influence of ZPs on the phase output voltage, fc1 and fc2 should be selected carefully so that P is a reciprocal of an integer. Moreover, other measures such as phase shift could be taken so that ZPs can fall into IPs. In this paper, considering generality, P=1 in this case. In order to simplify the analysis, quasi-180o square modulation is applied to the half-bridge DC-DC converter and only ZP effect caused by dead time is taken into account.

## Average mathematical model of output voltage without optimization

Define Vdc as the DC input voltage, N as the transformer’s ratio, k as the real-time value of modulation wave for 3-VSI, T1 and T2 as the carrier periods of DC-DC converter and 3-VSI, respectively, T0 as the fundamental period of 3-VSI. Taking phase a of FDCLI as an example, the average of output phase voltage over one carrier period (T2) according to Fig. 2 is given as

(2)

However, the existence of ZP in DC-Link voltage causesto change, which is relevant with the difference between fc1 and fc2 and the real-time value of 3-VSI modulation wave.

Before taking any measure of optimization, the following assumptions are made for the simplification of analysis:

-- With different values of P, the point where the carriers of DC-DC converter and 3-VSI coincide is always at the negative peak;

-- The segmented ZPs are distributed evenly in the positive and negative region of phase voltage;

Fig. 3 shows four typical voltage waveforms of phase a with different k values when P=1. Since dead time zone is often generated from the time delay on the rising edge of triggering signals of IGBTs in the same leg [19], the areas of ZPs start from the time spot of carrier zero crossing. In Fig.3, tz is the duration of ZP, ((is the ratio of tz to the carrier period of 3-VSI (T2).

Fig. 3. Waveforms of ua under different values of k with P(=(1

It can be seen from Fig.3 that all ZPs are in the positive voltage region when k(=(u*a1, and the average of output voltage is reduced. When k(=(u*a4, all ZPs are in the negative voltage region, so that the average of output voltage is increased. When k(=(u*a2, the average output voltage is reduced because of the existence of critical point (CP). When k(=(u*a3 a similar phenomenon appears but ends up with a contrary result. Further analysis reveals that all CPs exist in the right side of ZPs, as shown at the CPs in Fig.3, and.

The values of under different k values are given in (3). It is clear that the existence of CPs seriously affects ZPs without carrier’s phase-shift, and the average output voltage is affected in the meantime.

(3)

## Average mathematical model of output voltage with phase-shift optimization

According to the analysis based on Fig. 2, the influence of ZPs on the output voltage could be reduced by the careful configuration of the phase difference between carriers of DC-DC converter and 3-VSI. Therefore, if the number of ZPs that are distributed in the positive voltage region inside T2 equals to that distributed in the negative region, the influence of ZPs is minimized. This paper proposes an optimization scheme, where the ZPs are distributed evenly in positive and negative voltage region by shifting the phase of 3-VSI carrier. As shown in Fig.4, by phase shifting the ZPs can be evenly distributed in the both sides of the negative peak of 3-VSI voltage. In this case, the phase-shift is, which is not related to the value of P.

Fig. 4. Waveforms of ua under phase-shift carrier and different values of k with P(=(1

After phase shift, CPs only exist when the value of k is big enough. It is clear with further analysis of Fig. 4 that CPs are distributed symmetrically about the peak of carrier at a time distance of tz/2, and |k|(=(1(((2(. Taking the CPs as a reference, the average output voltages under all the circumstances can be written as

(4)

By comparing (3) and (4), it is clear that the influence of ZPs on average output voltage is reduced, and is eliminated when k((([-1+2a, 1-2a). Moreover, ZPs can only be divided when the value of k is big enough. In this case, ZPs are located in the IPs of 3-VSI, i.e., in the zero vector voltage, which helps the realization of soft switching of DC-DC converter.

## Fourier analysis of voltage difference after optimization

The average mathematical model offers intuitive explanation of the instantaneous effect of ZPs in one carrier period on output voltage. However, the model fails to explain the effect of ZPs in one modulation wave period. Here, the analytical mathematical model based on the Fourier series of f((t) is utilized for analysis, which is the time-varying function of output voltage bias and can be expressed as

f((t)(((fo(t)(((fa(t)      				                (5)

where(fo(t) is the time-varying function of FDCLI output voltage, and fa(t) is the time-varying function of PDCLI output voltage.

Fig. 5 shows the waveform of output voltage bias after being optimized with the carrier’s phase shift according to Fig. 4. For simplification, only the case of is discussed here, where  is a multiple of four and the negative peak of the carrier shares the same phase angle with the modulation wave (sinusoidal) of phase a.

Fig. 5. Example waveform of different voltage after phase-shift optimization for P=1

According to the Fourier series, the output voltage bias in Fig. 5 can be expressed by the sum of its harmonic contents as

(6)

where n is the order of harmonics, ( is the fundamental frequency of output voltage in rad/s.

ZP will not be segmented when |k|(≤((1(((2((), and the voltage difference is distributed evenly in the positive and negative parts, which is called half-cycle symmetry. The Fourier coefficients are as follow

(7)

Which shows that under these circumstances DC bias does not exist, so is the case of sinusoidal harmonic component. However, the phase and amplitude of cosine component are affected by ZPs, and the effect is related to the value of (.

The Fourier series of DC bias becomes complex because ZPs are segmented when 1>|k|(>((1(((2((), as shown in Fig.5. Under this circumstance, the voltage difference is quarter-cycle symmetrical and there is no cosine component in Fourier series (i.e.). Then the Fourier coefficients can be rewritten as (8). Where M is modulation index, n is odd, q is the number of half-period between the positive peak of the carrier and π/2 or the negative peak of the carrier and 3π/2. is the amplitude of modulation wave at the peak of the qth carrier. corresponds to the voltage difference where ZPs are not segmented, and  corresponds to the voltage difference where ZPs are segmented.

(8)

It can be seen fromthat the deviation of DC voltage offset is no longer zero and is decided by the width difference of ZPs that are segmented near π/2 and 3π/2. However, the areas near π/2 and 3π/2 are very small, therefore the resulting deviation of DC voltage offset is not large, especially in the cases with a small modulation index. It can also be observed from the characteristic comparison and experimental results given in the following part.

The deviation of DC voltage offset is affected greatly by ZPs that are not segmented, which could be seen in . The value of  is not very large because ZP width is very small. The effect of segmented ZPs is also not very serious. The segmentation is generated on the carrier’s peak after phase shift, which is also in the IP of phase voltage. This implies that deviation harmonics of voltage bias could be reduced by carrier’s phase shift.

Nonetheless, after the carrier’s phase shift, the DC bias of voltage difference still exists but the offset value is not very large, and the harmonics of segmented regions are not seriously affected by ZPs. It should be noted that only the qualitative analysis is provided above on the time-varying function and mechanism of the voltage difference caused by each ZP alone. Different kinds of ZPs are actually included in one fundamental period, so that the actual combined action is more complex. Quantitative analysis and comparison are carried out with time-domain simulation results.

# Comparison of Output Performances with Zero Portion

To judge globally the effect of carrier phase-shift and ZP on AC phase output voltage, the following comparison between system characteristics with and without carrier phase-shift is carried out in terms of integral harmonic performance, DC voltage utilization ratio, and DC bias. The simulation and calculation of carrier phase-shift scheme is under P=1, tz(((10((s and different ZP widths.

## Comparison of total harmonics

Weighted total harmonic distortion (WTHD) [14] is adopted to judge the effect of harmonics of different order with higher accuracy. Fig. 6 shows the variation curve of WTHD against M.

It can be seen from Fig. 6(a) that ZP affects greatly the harmonic performance of output voltage, which is improved greatly after being optimized by carrier phase-shift and thus becomes similar with that without ZPs.

(a)

(b)

Fig. 6. WTHD with different M for (a) different control methods and (b) different ZP duties

(a)

(b)

Fig. 7. DC voltage utilization with different M for (a) different control methods and (b) different ZP duties

The effect of varying ZP width on harmonic performance of output voltage is shown in Fig. 6(b). WTHD decreases with the increase of ZP width when M((((1(((2((). WTHD increases with the increase of ZP width when M>(1(((2((), and the turning point moves forward gradually. It could be observed that WTHD is reduced below that without ZP when M is relatively small. This is unreasonable. Further comparison of simulation data reveals that very few sideband harmonics could increase or decrease, which is caused by the fact that pulse number in the sequence is increased due to the output voltage segmented by ZPs. The increased pulse number then increases calculation error greatly, and the sensitivity of WTHD against M is too high, therefore WTHD is abnormally reduced. However, this phenomenon does not affect the analysis of the WTHD resulted from ZPs.

## Comparison of DC voltage utilization ratio

Given that kudc is the DC voltage utilization ratio of Vob, which is fundamental wave amplitude, to a half of DC-Link voltage, i.e. .The calculation result is shown in Fig. 7.

It can be seen from Fig. 7(a) that kudc is reduced by ZPs, and is increased with carrier phase-shift, which is similar with the case without ZPs.

Fig. 7(b) shows the kudc with different ZP widths. ZP width variation has nearly no effect on kudc when M((((1(((2((), while the negative discrepancy of kudc increases gradually with the increase of ZP width when M(>((1(((2((), and the turning point moves forward gradually, too.

## Comparison of DC bias

Given that the DC bias (symbolized by kbdc is calculated by the ratio of Vobdc, which is DC bias of phase voltage, to half of DC-Link voltage, i.e. , the calculation result is shown in Fig. 8.

(a)

(b)

Fig. 8. DC bias with different M for (a) different control methods and (b) different ZP duties

It can be seen from Fig. 8(a) that kbdc is increased by ZPs, and is reduced with carrier phase-shift, which is similar with the case without ZPs.

Fig. 8(b) shows that average DC bias over one modulation period is basically zero when M((((1(((2(() and with carrier phase-shift, due to the fact that the ZPs in positive and negative voltage regions are symmetrical. ZPs begin to be segmented when M(>(1(((2((), but don’t affect kbdc seriously.

In other words, carrier phase-shift strategy could improve harmonic performance of output voltage when certain distribution condition of ZP is satisfied, so is the case of DC voltage utilization ratio and DC bias. By these means, the problem caused by ZPs is eliminated to some extent, and the realization of soft-switching of DC-DC converter is easier.

# Simulation and Experimental Validation

The power circuit model and control layout of PDCLI are built in MATLAB, and a prototype system with P=1 is also settled in the lab to verify the the analysis and optimization strategy. The parameters used in simulation and field experiment are listed in table I.

## Simulation validation

The simulation is carried out mainly when M(=(0.5 and 0.9. For convenience, the amplitudes of output voltages under these two M values are kept substantially similar by adjusting the input voltages to different values. The filter parameters are also the same in both cases, hence Lf=0.875mH, Cf=(650F.

TABLE I

Validation Parameters

| Fundamental frequency f0 | 50Hz |
| --- | --- |
| Carrier frequency fc2 | 4kHz |
| Zero portion duty tz | 20(s |
| DC voltage Vdc | 1000..2000V |
| Transformer ratio N for Simulation/Experiment | 2 / 1.15 |
| Load power | 10kVA |

TABLE II

simulated Result Comparison under Different Situations

| System | P | SPWM Conditions | Output Phase Voltage |
| --- | --- | --- | --- |
|  |  |  | M=0.5 | M=0.9 |
|  |  |  | Mag. (V) | THD (%) | Mag. V | THD % |
| FDCLI | any/80 | no ZP | 360.4 | 3.364 | 360.8 | 1.006 |
| AI-HM based PDCLI | 80/80 | with ZPs | 248.7 | 19.854 | 241.4 | 3.743 |
|  |  | Phase-shift | 357.8 | 3.376 | 352.8 | 0.903 |

TABLE III

Performance Comparison under Different Load Situations

| Load Type | R | R//L | R//C | R//L | R//C | Diode |
| --- | --- | --- | --- | --- | --- | --- |
| uus | 358 | 359 | 368.7 | 400.5 | 413.6 | 359 |
| PF | 1.0 | 0.85 | -0.85 | 0.12 | -0.12 | 1.0 |
| THDiu/% | 3.7 | 3.5 | 12.1 | 3.34 | 21 | 30.8 |
| THDuus/% | 3.7 | 3.1 | 3.7 | 1.3 | 3.5 | 2.43 |

Here gives the simulation results of M(=(0.5 for example. Fig. 9(a) shows the simulation result without any optimization strategy, and Fig. 9(b) shows the result with carrier phase shift optimization. Table II and Table III shows the comparison results among different control methods and different load types, respectively.

From the simulation results, it can be concluded that ZPs obviously affect the amplitude and harmonic characteristics of the output voltage, especially in the case when M is relatively smaller. The optimization of carrier phase-shift reduces the ZP effect on output voltage, and the performance of the output voltage is improved greatly. Take M=0.5 as an example, the amplitude is increased to 357.8V and THD reduced to 3.376%, which are quite similar with the case without ZPs. It can also be derived from Table III that after phase-shift optimization, the THD of phase voltage would not become worse under different load types with different power factors; but the amplitude will be boosted under loads of very low power factors if open loop without any compensation is used for phase voltage control, which will hardly happen for railway auxiliary inverter applications, where non-linear and induction loads with power factors between 0.5 to 1.0 are much more popular.

According to IEC61287-1 and other related railway  standards, 30% and 70% dynamic load test can be performed and the result is given in Fig. 10. It can also be seen that the system performances very well for dynamic load with variation of 70%.

The simulation results validate theoretical analysis, the accuracy of mathematical model, the rationality of ZP effect analysis, and the practicability of carrier phase-shift strategy.

## Experimental validation

A test system using existing components as shown in Fig. 11 is built in lab, which is equipped with digital control layout with DSP. The DC-DC converter consists of IGBTs, high-frequency rectifying diodes, and ferrite-core transformer. The 3-VSI consists of IPM with existing output LC filter of  Lf(((1.3mH and Cf(50(F.

Fig. 12 and Fig. 13 give the experimental waveforms with carrier phase-shift optimization, and Table IV shows the comparative results. Fig. 12 shows the typical triggering waveform with carrier phase-shift optimization strategy. In this case, the ZPs are distributed symmetrically in positive and negative voltage regions over one carrier period of T2. Fig. 13(a) and Fig. 13(b) shows the 3-phase output voltage waveforms and harmonic spectrum of PDCLI without and with optimization, respectively. The 3-phase output voltage waveforms and harmonic spectrum are improved greatly with optimization than that without optimization. The voltage RMS value is increased to 220.1V, and THD is reduced to 2.6%, which are very similar with the case without ZPs and thus validates the proposed optimization scheme.

The system efficiency under given power is also compared with that of FDCLI and shown in Fig. 14. It can be derived that the efficiency controlled by the proposed AI-HM PDCLI is higher than that of FDCLI within the whole input DC voltage range: at least 2% at the worst case with low input voltage. It can also be seen that the efficiency of the proposed PDCLI increases, while the efficiency of FDCLI decreases as the Vdc increases. For the proposed PDCLI, the driving pulses of front-end DC-DC don’t change to regulate the DC-link voltage that the DC-DC loss keeps nearly stable; which results the amplitude increasing of the pulsating DC-link voltage, and  the on-state loss reducing of the 3-VSI. Then the overall efficiency increases. But for FDCLI, the loss of 3-VSI will keep stable for the stable DC-link voltage, but as the input voltage increases, the switching loss increases, which is greater than the decreasing of on-state loss, so the overall efficiency is reduced.

Fig. 10.  Dynamic performance with changing load

Fig. 11.  Hardware test platform

Fig. 12. Experimental drive pulses for phase-shift

Fig. 14. System efficiency comparison under rated power

TABLE IV

Experimental Result Comparison under Different Situations

| System | P | SPWM Conditions | Output RMS Phase Voltage |
| --- | --- | --- | --- |
|  |  |  | Mag. (Vrms) | THD (%) | DC bias (%) |
| FDCLI | any/80 | no ZP | 224.3 | 2.8 | 0.9 |
| AI-HM based PDCLI | 80/80 | with ZPs | 181.5 | 10.1 | 1.2 |
|  |  | Phase-shift | 220.1 | 2.6 | 1.1 |

# Conclusion

This paper analyzes the mechanism of the ZP effects on the output voltage of the AI-HM-based railway auxiliary inverter with pulsating DC-link, an optimization strategy of carrier phase-shift is proposed to reduce the influence of ZPs. The following conclusions are drawn from the average mathematical model of output voltage, the Fourier series of voltage bias, time-domain simulation results and experimental results:

--The proposed PDCLI is simplified by eliminating the LPF, and no additional commutation semi-conductors are needed, the efficiency and output voltage performance is improved by using carrier phase-shift to the simple AI-HM for railway auxiliary inverters. And as the Vdc increases, the efficiency of the proposed PDCLI increases, while the efficiency of FDCLI decreases.

--ZPs affect harmonic contents of output voltage seriously, and affect DC voltage utilization ratio and DC bias to some extent.

--With carrier phase-shift optimization strategy, ZPs are distributed more on the positive and negative peaks of output carrier. The even distribution of ZPs around carrier peaks when ZPs are segmented inside the ideal portion of phase voltage reduces the effect of ZPs on output voltage, which is similar with the ideal output.

References

Martinez C，Lazaro A，Lucena C，et al, “Improved modulator for losses reduction in auxiliary railway power supplies,” Applied Power Electronics Conf.  and Exp.，California，USA，2013．

L. J. Diao, J. Chen, W. Lin and Z. Liu, "Analysis and design for reducing voltage stress in output rectifier of LFLRV SIV DC-DC converter," IEEE International Symp. Industrial Electronics, Seoul, pp. 1077-1080, 2009.

Porzio M，Frasca R，Cascone B，et al．“Modern soft-switching topology for galvanic insulated railways auxiliary converter,” Conf. Power Electronic，Electrical Drives，Automation and Motion，Pisa，Italy，2010．

Vinnikov D．Research，design and implementation of auxiliary power supplies for the light rail vehicles．Tallinn Univ. Technol., Department of Electrical Drives and Power Electronics, Tallinn, Estonia, PhD dissertation, 2005．

J. Chen, L. J. Diao, L. Wang, H. Du and Z. Liu, "Distributed Auxiliary Inverter of Urban Rail Train—The Voltage and Current Control Strategy Under Complicated Load Condition," IEEE Trans. Power Electronics, vol. 31, no. 2, pp. 1745-1756, Feb. 2016.

Mazumder S K，Rthore A K, “Impact of DC link pulse coding on the harmonic distortion of the high-frequency-link inverter,” 36th Annual Conf. on IEEE Industrial Electronics Society，Glendale，AZ，USA，2010．

Prasanna U R，Rathore A K, “A Novel Single-Reference Six-Pulse-Modulation (SRSPM) Technique-Based Interleaved High-Frequency Three-Phase Inverter for Fuel Cell Vehicles,” IEEE Trans. Power Electronics，vol. 28, no. 12, pp.5547-5556, 2013．

Prasanna U. R. and Rathore A. K., "Dual Three-Pulse Modulation-Based High-Frequency Pulsating DC Link Two-Stage Three-Phase Inverter for Electric/Hybrid/Fuel Cell Vehicles Applications," IEEE Journal of Emerging and Selected Topics in Power Electronics, vol. 2, no. 3, pp. 477-486, Sept. 2014.

Chen L，Amirahmadi A，Zhang Q，et al．, “Design and implementation of three-phase two-stage grid-connected module integrated converter,” IEEE Trans. Power Electronics，vol. 29, no. 8, pp. 3881-3992, 2014．

Wen H，Xiao W，Wen X，et al．,“Comparative evaluation of DC-link capacitors for electric vehicle application,” Sustainable Energy，Hangzhou，China，2012．

Baburaj K，Vassilios G A，Josep P, “Performance evaluation of three-phase grid-connected photovoltaic inverters using electrolytic or polypropylene film capacitors,” IEEE Trans. Sustainable Energy，vol. 5, no. 4, pp. 1297-1306, 2014．

De D, Ramanarayanan V, “Analysis, Design, Modeling, and Implementation of an Active Clamp HF Link Converter,” IEEE Trans. Circuits and Systems, vol. 58, no. 6, pp. 1446-1455, 2011.

Holmes D G, Lipo T A. Pulse width modulation for power converters: principles and practice. John Wiley & Sons, 2003.

M. Sharifzadeh, H. Vahedi, R. Portillo, M. Khenar, A. Sheikholeslami, L. Franquelo,et al., "Hybrid SHM-SHE Pulse-Amplitude Modulation for High-Power Four-Leg Inverter," IEEE Trans. Industrial Electronics, vol. 63, no. 11, pp. 7234-7242, Nov. 2016.

M. Sharifzadeh, H. Vahedi, A. Sheikholeslami, P. A. Labbé and K. Al-Haddad, "Hybrid SHM-SHE Modulation Technique for a Four-Leg NPC Inverter With DC Capacitor Self-Voltage Balancing," IEEE Trans. Industrial Electronics, vol. 62, no. 8, pp. 4890-4899, Aug. 2015.

A. Rahnamaee and S. K. Mazumder, "A Soft-Switched Hybrid-Modulation Scheme for a Capacitor-Less Three-Phase Pulsating-DC-Link Inverter," IEEE Trans. Power Electronics, vol. 29, no. 8, pp. 3893-3906, Aug. 2014.

A. Rahnamaee, H. Riazmontazer, A. Mojab, S. K. Mazumder and M. Zefran, "A Discontinuous PWM Strategy Optimized for High-Frequency Pulsating-DC Link Inverters," IEEE Applied Power Electronics Conf. and Exp. (APEC), Charlotte, NC, 2015, pp. 849-853.

De D，Ramanarayanan V, “A proportional+multiresonant controller for three-phase four-wire high-frequency link inverter,” IEEE Trans. Power Electronics，vol. 25, no. 4, pp. 899-906, 2010．

Z. F. Ming, M. C. Zhou, “Impact of zero-voltage notches on outputs of soft-switching pulse width modulation converters,” IEEE Trans. Industrial Electronics, vol. 58, no. 6, pp. 2345-2354, 2011.

De D, Ramanarayanan V, “A dc-to-three-phase-ac high- frequency link converter with compensation for nonlinear distortion,” IEEE Trans. Industrial Electronics, vol. 57, no. 11, pp. 3669-3677, 2010.

H. Q. Du, L. J. Diao, Z. Y. Zhou, etc., “Zero portion effects and compensation of three phase inverters with the pulsating DC-link,” Proc. CSEE, vol. 36, no. 1, pp.: 205-214, 2016.

Texas Instruments, TMS320x2833x, 2823x Enhanced Pulse Width Modulator (ePWM) Reference Guide (Rev. A). Reference Guide, SPRUG04A, July, 2009.

# Footnotes

Manuscript received February, 2017. This work was supported in part by the China National Science and Technology Support Program under Grant 2013BAG21Q00, 2015BAG13B01, and China Scholarship Council.

Lijun Diao, Lei Wang (corresponding author), and Zhigang Liu are with the School of Eletrical Engineering, Beijing Jiaotong University, Beijing, 100044, China (e-mail: ljdiao, leiwang, zhgliu@ bjtu.edu.cn).

Huiqing Du is with CSSC System Engineering Research Institute, Beijing, 100094, China (e-mail: 11117361@ bjtu.edu.cn).

Lu Wang, Suleiman M. Sharkh are now with the Faculty of Engineering and Environment, University of Southampton, SO17 1BJ, UK (e-mail: lw5g13, s.m.abu-sharkh@soton.ac.uk).

# Text boxes

Fig. 9. AI-HM Simulation waveform and harmonic spectrum of output voltage for P=80/80 and M=0.5 (a) without any ZP optimization and (b) under phase-shift optimization

Fig. 13.  AI-HM experimental waveform and harmonic spectrum of PDCLI output rms voltage for P=80/80 and M=0.9 (a) without any ZP optimization and (b) under phase-shift optimization