## Slide 1: Test Chip 02 Testboard Design
By Kang

## Slide 2: Architecture

## Slide 3: Checklist
Rectifier test
  Vout vs Vin (Both manual and self-tuning)
  Efficiency vs Vin
LC-tune test
  Self tune and manual tuning
PLL test
  Data demod vs Q factor (BER, max. data rate)
PMU test
  3V DC output, power

## Slide 4: Requirement for testing
LC tank with variable series resistance for selectable Q
Random serial-bit data generator, TX driver, TX LC tank
Data logic analyser to PC
Debug configuration circuit
Int. Amp for very weak current measurements
Variable DC voltage reference generator for PLL demodulation setting

## Slide 5: Test board system diagram
Requirement:
Current probe circuit
Debug config Control
Vref generator
Logic analyser circuit
Local supply (both positive and negative)

## Slide 6: Rectifier test
Test
Vout vs Vin (Both manual and self-rectifier efficiency tuning)
Efficiency vs Vin
Vout cold start measurement
The input resistor is selectable.
Need large resistance to accurately measure rectifier input impedance
x

## Slide 7: LC-tune test
Test
Manual and self-tuning (resolution, accuracy, settling time)
Test inductor ~53uH (From previous measurement/calculation)
Series resistance and Q-factor (1MHz operating frequency)
  R = 50ohm , Q = 6.66
  R = 33ohm, Q = 10
  R = 3.3, Q = 100
  R = 2.22, Q = 150 ***assuming Rload = ∞ (or rectifier is off)
Series Resistance | Q-factor (@1MHz, L = 53uH)
50 | 6.66
33 | 10
10 | 33.3
5 | 66.6
3.3 | 100
2.22 | 150

## Slide 8: PLL/Data demodulation test
Test
Output data vs Q factor (BER, max. data rate)

## Slide 9: Test Board Complete Schematic

## Slide 10: Current probe circuit
INA121PA

## Slide 11: Debug configuration control and logic analyser

## Slide 12: Reference generator and Local Supply
Negative supply: LT1054IP (http://uk.farnell.com/texas-instruments/lt1054ip/dc-dc-conv-switched-capacitor/dp/2323589)
Opamp LM741CN TL081IP

## Slide 13: Comparator with Hysteresis
http://www.ti.com/lit/ug/tidu020a/tidu020a.pdf
R3 = 1Mohm
R1=R2=222Kohm

## Slide 14: List of parts
Slide switch SP3T http://uk.farnell.com/c-k-components/os103012mu1qp1/switch-slide-sp3t/dp/2435107
Inverters CD4069 http://uk.farnell.com/texas-instruments/cd4069ube/ic-4000-cmos-4069-dip14-18v/dp/1106113
INA121PA Instrumentation Amplifier http://uk.farnell.com/texas-instruments/ina121pa/ic-inst-amp-fet-600khz-dip8/dp/1648643
LN741CN OPAMP http://uk.farnell.com/texas-instruments/lm741cn/ic-op-amp-compensated-dip8-741/dp/9486780
Trimmer Potentiometer http://uk.farnell.com/bourns/3299w-1-103lf/pot-trimmer-10k-25-turn-3-pin/dp/9353704
Comparator Micropower MAX993ESD+ http://uk.farnell.com/maxim-integrated-products/max993esd/comparator-r-to-r-quad-300ns-nsoic/dp/2515111
IC socket http://uk.rs-online.com/web/p/plcc-sockets/1828231/

## Slide 15: PCB Layout

## Slide 16: TX/LC Driver board
List of component
Resistance 1 ohm (RS, 683-5616)
Zener diode (RS, 463-795) (654-7599)
MOS driver (RS, 774-7668)
MOSFET dual channel (RS,671-0356)
Resistor
MOSFET low side driver (RS,774-7674 and 668-4386)

## Slide 17: TX/LC Driver board
List of component
Resistance 1 ohm (RS, 683-5616)
Zener diode (RS, 463-795) (654-7599)
MOS driver (RS, 774-7668)
MOSFET dual channel (RS,671-0356)
Resistor
MOS driver (RS, 761-9585)
MOS NFET (RS, 708-5134)
Low side MOS driver (RS, 923-3836)
Low side MOS driver (RS, 403-840)
Dual side MOS driver (RS, 774-7674)

## Slide 18: TX/LC Driver board
List of component
Resistance 1 ohm (RS, 683-5616)
Zener diode (RS, 463-795) (654-7599)
MOS driver (RS, 774-7668)
MOSFET dual channel (RS,671-0356)
Resistor
MOS driver (RS, 761-9585)
MOS NFET (RS, 708-5134)
Low side MOS driver (RS, 923-3836)
Low side MOS driver (RS, 403-840)
Dual side MOS driver (RS, 774-7674)

## Slide 19: TX PSK pulse generator
List of component
Octal d-ff 74HC273D (RS, 113-0180)
Dual d-ff 74HCT74D (RS, 483-7878)
Quad XOR 74HC86D (RS, 112-6276)
Quad NOR 74HC02 (RS, 113-0095)
Multiplexer 1-of-2, (RS, 759-9330)
Dual 4-stage counter, (RS, 177-6865)

## Slide 20: TX PSK pulse generator
List of component
Octal d-ff 74HC273D (RS, 113-0180)
Dual d-ff 74HCT74D (RS, 483-7878)
Quad XOR 74HC86D (RS, 112-6276)
Quad NOR 74HC02 (RS, 113-0095)
Multiplexer 1-of-2, (RS, 759-9330)
Dual 4-stage counter, (RS, 177-6865)
Hex Inverter, (RS, 663-1607)
Quad NAND2, (RS, 663-2353)
5V REG, (RS, 298-8508)
18V REG, (RS, 516-6183)