# An optimization method for vibration suppression and energy dissipation of the axially moving string with hybrid nonclassical boundaries

Yuanfeng Wu1, Enwei Chen1 Neil. S Ferguson2, Yuteng He1, Haozheng Wei1, Yimin Lu1

1School of Mechanical Engineering, Hefei University of Technology, Hefei, 230009, China; 2Institute of Sound and Vibration Research, University of Southampton, Southampton S017 1BJ, UK

(Received May 19th, 2022; Revised Oct 21st, 2022; Accepted Nov 21st, 2022)

Keywords: Axially moving string; Nonclassical boundary; Bi-objective optimization design; Particle swarm optimization.

Correspondence to: Enwei Chen / cew723@163.com

----------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Abstract  The axially moving string model is widely used in engineering applications and is of great significance in research. In order to suppress the transverse vibration and facilitate energy dissipation of the axially moving string with nonclassical boundaries, a bi-objective optimization model and methodology are proposed for its boundary parameters’ design. First, an approximate numerical model for an axially moving string with a nonclassical boundary is established, which based on the finite element method (FEM) and Newmark-beta method. Then, a bi-objective model is proposed, including the average transverse vibration and the average system energy in a single traveling wave period, and a particle swarm optimization (BOPSO) algorithm is established for optimization. Finally, the proposed optimization model is applied in a numerical example, and the results are compared with NSGA-II, a multi-objective cuckoo search algorithm (MOCSA), and multi-objective flower pollination algorithm (MOFPA) to verify the feasibility of the proposed methodology.

----------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

1. Introduction

Axially moving systems, i.e., string, beam, conveyor belt, web, etc., play an important role in our life and modern industry, significantly contributing to promoting life quality and engineering development [1]. The axially moving string is considered the most fundamental and common model for axially moving systems, with a large volume of previous academic study [2]. Vital engineering devices, such as elevator and crane container systems, are typical applications of axially moving string models [3].

Since the 1950s, researchers have conducted extensive studies covering dynamics modeling methods of axially moving string systems [4]. Subsequently, numerous studies were performed, mainly focusing on different work conditions, materials and boundaries. Andrianov and Awrejcewicz [5] derived a governing equation of an axially moving string with time-varying velocity. Based on a varying-length string system, Zhu and Chen [6] investigated the forcing response of an elevator system. For a string comprising viscoelastic material, Chen [7] constructed its governing equation with the Boltzmann superposition law. More recently, Sorokin [8] studied the effect of viscous dampers on the dynamics of an axially moving non-uniform string with spatially periodically varying mass. Regarding a particular nonclassical boundary condition, Gaiko and van Horssen [9] investigated the low-frequency vibration of the axially moving string with a damper-spring-mass boundary. They also studied the vibrations of an elevator cable with a swayed boundary [10]. Based on an actuator at one boundary, the boundary control of an axially moving string is studied by Kim et al [11]. Lee et al. [12] studied the vibration characteristics of axially moving beam using the transfer matrix method. Moreover, the response of free oscillation with similar nonclassical hybrid boundaries was also studied by Chen et al. [13].

In terms of modeling methods, it can be divided into either approximate or analytical methods. Currently, approximate methods are widely employed to address the response of an axially moving string, wherein the Galerkin discretization method is a common choice [3]. For example, Chen et al. [14,15] adopted Galerkin truncation to study the vibration of the viscoelastic moving string as well as chaos and bifurcation phenomena. Yang et al. [16] analyzed the nonlinear vibration of an axially moving string using gyroscopic complex modes based on the Galerkin truncation and perturbation approach. Furthermore, some other approximate methods are introduced in this system, wherein the finite element method (FEM) is typical. Fung et al. [17] first applied FEM to solve the transverse vibration of a string with time-varying length, and Yao et al. [18] presented a hybrid Laplace transform/FEM for the same problem. Subsequently, Chen et al. [19,20] studied energy dissipation of the vibration of an axially moving string with simple and viscous damper boundaries using FEM. In addition to approximate methods, analytical methods have been recently employed. For instance, Chen et al. [21,22] developed a time-domain reflected wave superposition method to analyze energy dissipation and transverse vibration response of different nonclassical boundaries.

From the review above, the previous research mainly focused on complicated or hybrid boundary conditions, which are more complex than the simple fixed-support boundary condition. Most papers provide profound studies on the dynamic behavior in the dynamic analysis process. Nevertheless, few studies aim to explore the proper parameters configuration of hybrid boundaries for vibration suppression and energy dissipation, and it is a valuable issue. As a powerful tool for optimization, the intelligent evolution algorithm has been widely used in recent engineering design and industry [23]. To the best of the authors’ knowledge, no research has been conducted combining an intelligent algorithm applied to the axially moving string problem to determine the optimal parameter of the hybrid boundaries.

Compared with the approximate methods, an analytical method, e.g., the reflected wave superposition method, is more accurate. For the latter, though, once the boundary conditions change, its complicated dynamical model should be rederived; moreover, its computation efficiency is lower than that of the approximate method. In this paper, a method combining particle swarm optimization (PSO) and FEM is used to explore and determine the proper parameter setting for vibration suppression and energy dissipation.

The rest of the paper is organized as follows. In Section 2, an approximate numerical method based on FEM and Newmark-beta method and a bi-objective model is developed to measure the vibration and energy dissipation degree. In Section 3, an improved bi-objective particle swarm optimization (BOPSO) is represented and combined with the model mentioned above to establish a bi-objective optimization model. The feasibility of the proposed model and the performance of the BOPSO are verified in Section 4. Section 5 introduces the overall conclusions and future work.

## 2. A numerical modeling method for vibration suppression and energy dissipation

#### 2.1 Numerical modeling of axially moving string

In practice, the boundary of the moving string may not be the simple fixed-fixed case. Typically, the complicated operating condition could be represented by a hybrid boundary comprising damping, mass, and spring. In this paper, a typical model with nonclassical boundary [9,10,13,22] is chosen and shown in Fig. 1, wherein  is the axial speed of the string,  denotes the distance of two ends,  is the transverse displacement of the string at instance  and position . The variables , , and represent the attached damping, mass, and stiffness at the right-side terminal. Besides, we suppose boundary mass m0, spring k0, and damping c0 do not have other properties. For instance, the damping c0 is regarded as a zero-mass and zero-stiffness damper.

To simplify the approximate model, the following classical assumptions are considered [13,19]: (a) The transverse vibration  is small; (b) The cross-sectional area , the linear mass density , elastic modulus , and tension  remain constant during the traveling process; (c) The axial speed  is smaller than that of the free wave propagation speed , where ; (d) The axial vibration is neglected.

Fig. 1. The schematic of an axially moving string with nonclassical hybrid boundary

For the system shown in Fig. 1, we suppose that the lumped mass  is initially at the equilibrium position, and its kinetic energy Ek and potential energy Ep are denoted in Eqs. (1)-(2).

|  | (1) |
| --- | --- |
|  | (2) |

where , and  denote the partial derivatives of the transverse displacement  with respect to time  and axial coordinate , respectively. Discretizing the string model by FEM, the transverse displacement of the -th element of the string can be approximated as shown in Eqs. (3)-(5):

|  | (3) |
| --- | --- |
|  | (4) |
|  | (5) |

where  is the shape function of the -th element [17,18];  is the number of the total elements of the discretized string;  is the nodal vector consisting of the transverse displacement of both sides of the -th element.

In particular, for the node vector  to , their kinetic and potential energy expressions are the first term of Eq. (1) and the first two terms of Eq. (2), respectively. Then, substitute Eqs. (3)-(5) to Eqs. (1)-(2), the Lagrangian of the -th () element can be obtained as follows:

|  | (6) |
| --- | --- |
|  | (7) |

where Ek,i and Ep,i are the kinetic energy and potential energy of the -th element, respectively; , , and  are 2×2 square matrices, and  is the nonlinear term of which the expressions are given in Eq. (7).

Based on the Lagrangian function, e.g., Eq. (8), the approximate model for element  can be derived as denoted in Eqs. (9)-(10):

|  | (8) |
| --- | --- |
|  | (9) |
|  | (10) |

where , . Note that the superscript “ ' ” represents the derivatives with respect to time. For the last node vector , according to the right boundary, we substitute Eqs. (1)-(2) into Eq. (11),

|  | (11) |
| --- | --- |

where  is the nonconservative force acting on the -th node, and obtain ,  and  (see Eq. (12)).

|  | (12) |
| --- | --- |

The governing equation has been transformed into an ordinary differential equation using the FEM approach, which is only related to time  and is independent of the axial coordinate . Combining with Eq. (9) of each element, the governing equation (see Eq. (13)) of local coordinate  can be derived.

|  | (13) |
| --- | --- |

where , , , .

For two adjacent elements  and , continuity conditions shall be satisfied. By reference [19], Eq. (13) can be transformed into Eq. (14) expressed in the global coordinates , namely the approximate transverse vibration of an axially moving string with nonclassical fixed-damper_spring_mass boundary, and its nonlinear term  is shown in Eq. (15).

|  | (14) |
| --- | --- |
|  | (15) |

For simplicity, when the nonlinear terms are small, i.e., considering assumptions (a) and (b), the linear model can be used as follows [19]:

|  | (16) |
| --- | --- |

Then, based on the improved Newmark-beta method [19], an approximate model of the axially moving string system, incorporating the approximate discrete model and numerical method of an axially moving string, is established, and the vibration response of any time interval can be calculated.

#### 2.2 The bi-objective model of the axially moving string system

For a linear model in Eq. (16), the traveling wave period  for an axially moving string means the minimum time to return its initial deflection shape, and the mathematical formulation of traveling wave period  is given in Eq. (17) [21].

|  | (17) |
| --- | --- |

In this subsection, two indicators in , namely the average vibration magnitude () and average energy () for the system indicators, are established to evaluate the system's vibration suppression and energy dissipation in a traveling wave period .

(1) The average vibration magnitude in . The transverse vibration is a significant factor impacting the smoothness and stability of the axial movement, particularly in precision machinery and other industrial applications [3]. Hence, an indicator used to measure the vibration suppression ability is developed, as expressed in Eq. (18),

|  | (18) |
| --- | --- |

where  is the vibration magnitude of the initial defection shape. Eq. (18) means the average transverse vibration magnitude of the axially moving string in the traveling wave period , which can be calculated by the approximate model in Section 2.1.

(2) The average energy in . The energy of transverse motion is also a critical factor influencing the stability of the string. The modal coordinate system evaluation method was adopted to study the energy caused by transverse vibration of the linear model (see Eq. (16)) as reported in the literature [19,20]. Firstly, calculate the eigenvector  and eigenvalue  of , and get the modal matrix . Then, the kinetic energy Ek and potential energy Ep of the proposed approximate model can be expressed as follows:

|  | (19) |
| --- | --- |
|  | (20) |

where  is the displacement modal coordinate, a time-dependent variable, an ,  are modal mass matrix and modal stiffness matrix, and the average energy index can be denoted in Eq. (21).

|  | (21) |
| --- | --- |

where E(0)= Ek(0)+Ep(0) is the system’s initial energy at =0.

Finally, the two objectives above are converted into a minimization requirement for optimization, as denoted in Eq. (22),

|  | (22) |
| --- | --- |

## 3. The bi-objective optimization modeling based on particle swarm optimization

This section introduces a bi-objective optimization model based on improved bi-objective PSO (BOPSO) in Sections 3.2 and 3.3. PSO, a well-known meta-heuristic algorithm, has been widely used in optimization algorithms due to its excellent performance in numerous optimization problems. It has desirable characteristics, such as fewer control parameters and easy implementation [24], and is adopted herein.

#### 3.1 Bi-objective optimizer and hypervolume indicator

The multi-objective optimization aims to find a solution X=[x1,…,xp] from the feasible domain . It considers an objective function vector  to obtain the optimal value, which shall satisfy the Eq. (23):

|  | (23) |
| --- | --- |

where X=[x1,…,xp] is the feasible solution composed of p design variables, and is the objective vector consisting of s objectives of the feasible solution;  and  denote the number of inequalities and equations. Note that ,  in this bi-objective optimization sequence model: .

Some scholars rank the objective and compare each objective one by one throughout the optimization process, i.e., the lexicographical method [23]. Furthermore, some studies are based on dimensionless parameters and weighting to transform multi-objective into a single objective function [25,26]. However, it is difficult to remove the unit among the different objective functions and optimize all the objectives to reach the best value simultaneously due to the conflict of each objective. Once the importance of each objective changes, the optimization procedure should be re-implemented.

In addition, the Pareto-dominated relationship is widely used for solution comparison, which treats each objective fairly in the optimization process. For instance, if the solutions  and  satisfy Eqs. (24)-(25),  dominates  noted as . If no solution dominates ,  is a Pareto non-dominated or non-inferior solution, and all these solutions constitute the Pareto non-dominated set . Its objective values are called the Pareto front denoted as .

|  | (24) |
| --- | --- |
|  | (25) |

wherein  is the number of objective functions,  is the feasible domain.

To evaluate the quality of each solution, two indicators, the crowd distance metric (CDM) and Pareto rank (PR), were developed by Deb et al. [27], which is the core of the tournament selection mechanism. The CDM of  can be calculated by Eq. (26), where  is the number of solutions in the corresponding rank. It is worth noticing that CDM(X1)=CDM(Xq)=∞. If  and Xj satisfy Eq. (27) or (28),  dominates Xj, namely Xj. This paper also employs this mechanism for solution comparison.

|  | (26) |
| --- | --- |
|  | (27) |
|  | (28) |

Nevertheless, this procedure cannot measure the quality of the Pareto front. Here, the hypervolume indicator [28] is chosen as a performance metric measuring the quality of the Pareto non-dominated set, and it does not require the real Pareto front in advance, which can be expressed in Eq. (29) [29]:

|  | (29) |
| --- | --- |

where the  is the space covered by Pareto front  and reference point , and  is Lebesgue measure. It is worth noticing that the  cannot be changed when comparing with different Pareto fronts; otherwise, the hypervolume  is not comparable.

#### 3.2 Particle behavior and neighbor searching operator

In the PSO algorithm, each position is a feasible solution associated with a particle. A particle can alter its velocity to a better position by sharing with other particles. A particle explores its position  by changing the velocity  to approach the current optimal solution  and the global best solution . When  changes its velocity and finds a better solution (or called location) , update the solution of  with the better  till it reaches the iteration limit.

The velocity and solution updating of the (k+1)-th iteration can be represented as follows:

|  | (30) |
| --- | --- |
|  | (31) |

where  is the inertial constant, and ;  and  are acceleration constants, and , ;  is the velocity vector of  in the -th iteration;  is the optimal solution of particle swarm of the kth iteration. Note that the value ranges of , , and  are defined in the related literature [24].

In order to diversify the solution searching process, the two-point crossover operator and one-point crossover operator of genetic algorithm based on binary encoding and decoding technique are adopted in velocity updating, in which the symbol “(” is the crossover operator. Before introducing two kinds of crossover operators, the binary encoding and decoding mechanism is presented. Take a design variable  () from  as an example to demonstrate the binary encoding.

Step 1. Determine the value range  of  and the number of decimal p to be retained, and the range will be partitioned into  parts;

Step 2. Find a constant  that satisfies ;

Step 3. Calculate the corresponding decimal number ;

Step 4. Convert the decimal-coded  to binary-coded, and obtain a binary sequence  for crossover, i.e., dd=[b1,…,by] (). Similarly, the decoding procedure of  can be executed from Step 4 to Step 3 to get the real-coded .

(a)

(b)

Fig. 2. The schematic of two-point crossover operator and one-point crossover mechanism of the first design variable, i.e. , of  and : (a) one-point crossover operator and (b) two-point crossover operator.

and , as denoted in Fig. 2 (suppose =6), are taken as two feasible solutions, and a crossover operator is determined randomly. Then, the design variable  of  and  can be transformed into two binary-coded sequences. Finally, the shown crossover procedure will be executed according to the randomly generated crossover points.

#### 3.3 Improved bi-objective particle swarm optimization

To handle bi-objective optimization and obtain more Pareto solutions, this paper combines the PSO algorithm with multi-objective processing methods and preserves all Pareto non-inferior solutions in the optimization process. The termination condition of the algorithm is to reach the maximum number of iterations. The basic framework of the proposed improved bi-objective PSO (BOPSO) is illustrated in Fig. 3, and the detailed steps are as demonstrated in this subsection.

Fig. 3. The flowchart of the proposed improved hybrid PSO algorithm

Step 1: Initialize PSO parameters, including iteration limit , swarm size , iteration counter , an empty external file .

Step 2: According to the range of each variable, generate the particle swarm randomly and obtain the initialized particles’ position  and velocity .

Step 3: Update  with the Pareto non-inferior solutions . Based on the tournament selection mechanism, select the current optimal solution  from , and set it as the global optimal solution .

Step 4: If , execute Step 5; otherwise, terminate the procedure.

Step 5: If , get the trail velocity  and trial position  of particle  based on the neighbor searching introduced in Section 3.2; otherwise, go to Step 7.

Step 6: If , update the current position  and velocity  with  and , respectively; otherwise update  and  with  and . Then, obtain the current optimal  of the non-dominated solutions of {} and set .

Step 7: Let , and update  with the non-dominated solutions of .

Step 8: Select  from  by tournament selection and set , , and go to Step 7.

4. Numerical Simulations

In this section, in order to verify the practicality and the performance of the proposed methodology, including the approximate model and bi-objective optimization model, the initial displacement conditions and some necessary parameters of the string model are described by Eq. (32) [19] and Table 1.

|  | (32) |
| --- | --- |

Table 1. The parameters of the axially moving string

| Parameters | Values | Parameters | Values |
| --- | --- | --- | --- |
| l | 3 m | Δt | Ttw/500 |
| T0 | 10 N | A0 | 0.01 m |
| v0 | 0.2·c | EA | 3.2×104 N |
| ρ | 0.4 kg·m-1 |  |  |

#### 4.1 Numerical results and performance comparison of the methods

Three classical Pareto-based multi-objective optimization methods are introduced for comparison, i.e., NSGA-II [27,30], MOCSA [31], and MOFPA [32], to illustrate the optimization performance of BOPSO. We set the scope of three design variables, i.e., , , and are , , and , respectively. The number of the total elements of the discretized string  is 20 by referring [20]. And the numerical results retain four decimal places. The initial parameters of BOPSO are set as follows: iteration limit of each run =100, swarm size =50, external archive . The transcoding process is accurate to four decimal places. The swarm size and iteration limit of NSGA-II, MOCSA, and MOFPA are also set the same values as aforementioned. Based on the model introduced in Section 2, the response of each time step at a traveling wave period and two objective functions in Section 3.1 can be calculated. To measure the quality of the Pareto solutions obtained by each algorithm, the reference point  of hypervolume is set as (3,3).

Fig. 4. The hypervolume values of the listed methods for 30 trial iterations

Fig. 5. The iterative convergence of the four optimization methods

Fig. 6. The iterative convergence of the four optimization methods

Table 2. The computation time of each optimization method

| Method | The computation time |
| --- | --- |
|  | Min | max | avg |
| MOCSA | 3337.64 | 3430.89 | 3392.76 |
| NSGA-II | 1823.06 | 1859.87 | 1846.64 |
| MOFPA | 2411.85 | 2440.84 | 2422.95 |
| BOPSO | 2033.60 | 2086.25 | 2063.89 |

Each optimization method ran 30 times independently, and the hypervolumes of the Pareto front obtained by the corresponding optimization method are shown in Fig. 4. The optimization was programmed on Matlab 2021a and performed on a 3.8GHz CPU, AMD Ryzen 7 5800X, with 16 GB RAM. It can be observed that the maximum hypervolume of NSGA-II, MOCSA, MOFPA, and BOPSO are 6.25497, 6.18482, 6.21909, and 6.26011, respectively, and the optimization result of BOPSO is stable instead of changing severely. Then, the box plot is used for optimization performance stability analysis, and hypervolumes of 30 trials are depicted in Fig. 5. By removing outliers, the best optimization results of each optimization method remain unchanged, and BOPSO obtained the best hypervolume value. It is evident that the five critical points of BOPSO in the box plot are better than any other compared method and the hypervolume range of BOPSO is the smallest among these approaches, as shown in Fig. 5, proving that the proposed BOPSO produces the best optimization stability. Besides, the computation time of the trial iteration of each optimization time is listed in Table 2. It reveals that BOPSO is inferior to NSGA-II but better than MOFPA and MOCSA. However, it is still a stable and high-quality optimization method in terms of optimization performance, as in the above analysis.

As the four algorithms achieve the maximum hypervolume, the results are used to analyze the convergence speed for each algorithm, as shown in Fig. 6. It can be found that BOPSO and NSGA-II have the fastest convergence rate concerning hypervolume, and BOPSO also achieves the best hypervolume value. The numbers of iterations required by the four methods to converge are 31, 32, 75, 81 for NSGA-II, BOPSO, MOCSA, and MOFPA, respectively. From the above analysis, whether in the optimization quality and stability or the detailed optimization process, BOPSO has the best performance.

Table 3. The Pareto frontier of the four algorithms

| Method | Solution | f1 | f2 | Method | Solution | f1 | f2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| MOCSA | 1 | 0.79468 | 0.25987 | MOFPA | 1 | 0.73419 | 0.25327 |
|  | 2 | 0.76501 | 0.26290 |  | 2 | 0.75869 | 0.25203 |
|  | 3 | 0.77191 | 0.26001 |  | 3 | 0.74689 | 0.25243 |
|  | 4 | 0.76322 | 0.26305 |  | 4 | 0.73452 | 0.25287 |
| NSGA-II | 1 | 0.72498 | 0.25134 | BOPSO | 1 | 0.72320 | 0.25162 |
|  | 2 | 0.72535 | 0.25098 |  | 2 | 0.72481 | 0.25097 |
|  | 3 | 0.72465 | 0.25136 |  | 3 | 0.72332 | 0.25121 |
|  | 4 | 0.72514 | 0.25130 |  | 4 | 0.72391 | 0.25105 |
|  | 5 | 0.72526 | 0.25125 |  | 5 | 0.72767 | 0.25081 |
|  |  |  |  |  | 6 | 0.72323 | 0.25141 |

Table 4. The parameter design results

| Method | Solution | c0 | k0 | m0 | Method | Solution | c0 | k0 | m0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MOCSA | 1 | 2.14174 | 1.02387 | 0.00738 | MOFPA | 1 | 1.97865 | 0.17612 | 0.00376 |
|  | 2 | 2.01443 | 0.76254 | 0.02270 |  | 2 | 1.84749 | 0.00511 | 0.0007 |
|  | 3 | 1.92331 | 0.67178 | 0.01472 |  | 3 | 1.9282 | 0.1879 | 0.00201 |
|  | 4 | 1.98360 | 0.73196 | 0.02503 |  | 4 | 1.95158 | 0.06041 | 0.00306 |
| NSGA-II | 1 | 2 | 0.037 | 0.001 | BOPSO | 1 | 1.98465 | 0.00658 | 0.00112 |
|  | 2 | 2 | 0.05 | 0.001 |  | 2 | 1.98162 | 0.00827 | 0.00043 |
|  | 3 | 2.001 | 0.032 | 0.001 |  | 3 | 1.98751 | 0.00245 | 0.00111 |
|  | 4 | 1.995 | 0.037 | 0.001 |  | 4 | 1.9876 | 0.00999 | 0.00084 |
|  | 5 | 1.995 | 0.033 | 0.001 |  | 5 | 1.98119 | 0.00756 | 0.00018 |
|  |  |  |  |  |  | 6 | 1.9819 | 0.01739 | 0.00112 |

Table 5. The optimization results of each objective function

| Method | The average vibration (f1) | The average energy (f2) |
| --- | --- | --- |
|  | min | max | avg | min | max | avg |
| MOCSA | 0.76322 | 0.79468 | 0.77371 | 0.25987 | 0.26305 | 0.26146 |
| NSGA-II | 0.72465 | 0.72535 | 0.72508 | 0.25098 | 0.25136 | 0.25125 |
| MOFPA | 0.73419 | 0.75869 | 0.74357 | 0.25203 | 0.25327 | 0.25265 |
| BOPSO | 0.72320 | 0.72767 | 0.72436 | 0.25081 | 0.25141 | 0.25118 |

Fig. 7. The Pareto front of the four methods

Table 3 and Fig. 7 show the Pareto frontiers of the best hypervolume of each method. As shown in Fig. 7, the Pareto non-dominated solutions obtained by BOPSO have distributed results outside worse using NSGA-II, i.e., it occupies a higher Pareto rank and dominates that of NSGA-II according to the dominance concept introduced in Section 3.1. Table 4 shows the corresponding design results. Table 5 compares the results of the best Pareto front of each method in Fig. 7. Concerning the average of , compared with BOPSO, the solution obtained by MOCSA, NSGA-II, and MOFPA increased by 6.813%, 0.198%, and 2.652%. It means that the Pareto optimization results on the average vibration magnitude using BOPSO are better than that of the other methods. A similar effect also occurs on the average energy, decreasing the string’s vibration and facilitating the energy dissipation in a traveling wave period.

In all, no matter the performance comparison evaluated by hypervolume or the overall optimization effect of each objective function, BOPSO has the most stable optimization performance and the best optimization result for the two objective functions.

#### 4.2 Selection choice of the Pareto front and sensitivity analysis

However, due to the conflict of each objective function, it is almost impossible to achieve the best value of all the objectives, and one improvement may worsen other objectives. Based on Pareto non-dominated relationship, a preference will not be introduced into the optimization process. Still, it is necessary to compromise on each objective for choosing the solution from the Pareto front. As a well-known decision-making method, the analytical hierarchy process (AHP) balances the different objectives for decision-making, and it is chosen here. AHP can be conducted in the following steps [33]: (1) select dimensionless quantities for the unit of each objective; (2) judge the importance of each objective function and set weighting coefficients ; (3) integrate the multi-objective functions into a single objective by weighting.

|  | (33) |
| --- | --- |

Eq. (33) expresses the weighted objective of a possible vector Xj, where  and  are the maximum and minimum of  in the Pareto front. We treat and  as equally important, i.e., setting ==0.5, and the solution 4 should be selected, for which =1.9876 N·s/m, =0.0099 N/m, =0.0008 kg. A sensitivity test was carried out to test the optimization performance of each boundary parameter design, i.e., changing one parameter value while the other two parameters kept the obtained optimized values. The result is shown in Fig. 8.

(a)

(b)

(c)

Fig. 8. The sensitivity test of the objective function to each design variable: (a) =0.0099 N/m, =0.0008 kg, (b) =1.98760 N·s/m, =0.0008 kg and (c) =1.9876 N·s/m, =0.0099 N/m.  is represented by blue curve corresponding to left-sided vertical coordinate, and  is represented by orange curve corresponding to right-sided vertical coordinate.

As shown in Fig. 8, the influence of  and  on the averaged vibration magnitude and average energy is not evident in the outcomes when the changes to viscous damper are made. When the damper reaches ,  falls and then rises, and  occurs in a similar situation with a slower rate, which means that  reaches the approximate optimal value for an elastic spring and mass equal to  and . In Fig. 8(b) and (c), it can be found that both  and  increase continuously with the increased stiffness and mass at the right-side boundary, which indicates that the result obtained by the optimization method previously has a good performance in terms of stiffness and mass optimization, respectively. Due to the small value of  and , we also set =0, =0, =1.9876, and obtained =0.72871, =0.25111. In addition, the results of the optimal damper in related literature [22] are compared, which are equal to =0.72749, =0.25152. The results obtained are dominated by the BOPSO selected solution, which suggests that the effect of spring and mass does not exert a purely negative influence on the optimization of  and .

5. Conclusions

Since many engineering devices are the actual applications of axially moving systems, it is of great significance to study the dynamic behavior of this model. For a specific boundary model, this work mainly focused on a nonclassical hybrid boundary parameters design for vibration suppression and energy dissipation using BOPSO. The main contributions and novelties are as follows:

1. To solve the response at any time in a traveling wave period, the approximate mathematical model based on FEM and Newmark-beta method was established. On this basis, the bi-objective model was constructed for design variable optimization in terms of energy dissipation and vibration suppression.

2. An improved bi-objective optimization model based on particle swarm optimization was proposed for design variable configuration optimization, combining Pareto non-dominated relationship, and binary-coded crossover operator of genetic algorithm.

3. To verify the practicality and superiority of the proposed model and method, a numerical optimization simulation was conducted. The result demonstrates that the proposed methodology can reduce the average vibration, facilitate energy dissipation and perform better than three well-known algorithms in optimization.

Although the effectiveness of the proposed methodology has been verified, some limitations still exist. In this paper, free vibration is discussed, and forced vibration can be studied in the future. In addition, other nonclassical boundaries can be considered for research.

Acknowledgments

This work is supported by the National Natural Science Foundation of China under Grant No. 51675150 and 51305115, and Natural Science Foundation of Anhui Province Grant No. 2208085ME130.

References

[1] P. T. Pham and K. S. Hong, Dynamic models of axially moving systems: A review, Nonlinear Dyn. 100 (1) (2020) 315-349.

[2] K. S. Hong and P. T. Pham, Control of axially moving systems: A review, Int. J. Control Autom. Syst. 17 (12) (2019) 2983-3008.

[3] K. S. Hong, L. Q. Chen, P. T. Pham and X. D. Yang, Control of Axially Moving Systems, Springer Nature, Singapore, (2022).

[4] K. Marynowski and T. Kapitaniak, Dynamics of axially moving continua, Int. J. Mech. Sci. 81 (2014) 26-41.

[5] I. V. Andrianov and J. Awrejcewicz, Dynamics of a string moving with time-varying speed, J. Sound Vib. 292 (3-5) (2006) 935-940.

[6] W. D. Zhu and Y. Chen, Forced response of translating media with variable length and tension: Application to high-speed elevators, Proc. Inst. Mech Eng Pt K-J Multi-Body. Dyn. 219 (1) (2005) 35-53.

[7] L. Q. Chen, Principal parametric resonance of axially accelerating viscoelastic strings with an integral constitutive law, Proc. R. Soc. London Ser. A-Math. Phys. Eng. Sci. 461 (2061) (2005) 2701-2720.

[8] V. S. Sorokin, On the effects of damping on the dynamics of axially moving spatially periodic strings, Wave Motion. 85 (2019) 165-175.

[9] N. V. Gaiko and W. T. van Horssen, On the transverse, low frequency vibrations of a traveling string with boundary damping, J. Vib. Acoust. 137 (4) (2015) 041004.

[10] N. V. Gaiko and W. T. van Horssen, Resonances and vibrations in an elevator cable system due to boundary sway, J. Sound Vib. 424 (2018) 272-292.

[11] C. W. Kim, K. S. Hong and H. Park, Boundary control of an axially moving string: Actuator dynamics included, J. Mech. Sci. Technol. 19 (1) (2005) 40-50.

[12] J. W. Lee, J. Y. Lee and D. M. Lee, Free vibration analysis of axially moving beams using the transfer matrix method, J. Mech. Sci. Technol. 35 (4) (2021) 1369-1376.

[13] E. W. Chen, K. Zhang, N. S. Ferguson, J. Wang and Y. M. Lu, On the reflected wave superposition method for a travelling string with mixed boundary supports, J. Sound Vib. 440 (2019) 129-146.

[14] L. Q. Chen, W. J. Zhao and H. Ding, On Galerkin discretization of axially moving nonlinear strings, Acta Mech. Solida Sin. 22 (4) (2009) 369-376.

[15] L. Q. Chen, J. Wu and J. W. Zu, The chaotic response of the viscoelastic traveling string: an integral constitutive law, Chaos Solitons Fractals. 21 (2) (2004) 349-357.

[16] X. D. Yang, H. Wu, Y. J. Qian, W. Zhang and C. W. Lim, Nonlinear vibration analysis of axially moving strings based on gyroscopic modes decoupling, J. Sound Vib. 393 (2017) 308-320.

[17] R. F. Fung, P. H. Wang and M. J. Lee, Nonlinear vibration analysis of a traveling string with time‐dependent length by finite element method, J. Chin. Inst. Eng. 21 (1) (1998) 109-117.

[18] C. M. Yao, R. F. Fung and C. R. Tseng, Non-linear vibration analysis of a traveling string with time-dependent length by new hybrid Laplace transform/finite element method, J. Sound Vib. 219 (2) (1999) 323-337.

[19] E. W. Chen and N. S. Ferguson, Analysis of energy dissipation in an elastic moving string with a viscous damper at one end, J. Sound Vib. 333 (9) (2014) 2556-2570.

[20] E. W. Chen, M. B. Li, N. S. Ferguson and Y. M. Lu, An adaptive higher order finite element model and modal energy for the vibration of a traveling string, J. Vib. Control. 25 (5) (2019) 996-1007.

[21] E. W. Chen, Q. Luo, N. S. Ferguson and Y. M. Lu, A reflected wave superposition method for vibration and energy of a travelling string, J. Sound Vib. 400 (2017) 40-57.

[22] E. W. Chen, J. F. Yuan, N. S. Ferguson, K. Zhang, W. D. Zhu, Y. M. Lu and H. Z. Wei, A wave solution for energy dissipation and exchange at nonclassical boundaries of a traveling string, Mech. Syst. Sig. Process. 150 (2021) 107272.

[23] J. L. J. Pereira, G. A. Oliver, M. B. Francisco, S. S. Cunha and G. F. Gomes, A review of multi-objective optimization: Methods and algorithms in mechanical engineering problems, Arch. Comput. Methods Eng.  (2021) https://doi.org/10.1007/s11831-11021-09663-x.

[24] X. S. Yang, Nature-Inspired Optimization Algorithms, Elsevier, Oxford, (2014).

[25] Y. L. Wang, X. P. Qin, S. Huang, L. Lu, Q. K. Zhang and J. W. Feng, Structural-borne acoustics analysis and multi-objective optimization by using panel acoustic participation and response surface methodology, Appl. Acoust. 116 (2017) 139-151.

[26] H. Zhu, Y. M. Hu, W. D. Zhu and Y. J. Pi, Optimal design of an autotensioner in an automotive belt drive system via a dynamic adaptive PSO-GA, J. Mech. Des. 139 (9) (2017) 093302.

[27] K. Deb, A. Pratap, S. Agarwal and T. Meyarivan, A fast and elitist multiobjective genetic algorithm: NSGA-II, IEEE Trans. Evol. Comput. 6 (2) (2002) 182-197.

[28] J. Bader and E. Zitzler, HypE: An algorithm for fast hypervolume-based many-objective optimization, Evol. Comput. 19 (1) (2011) 45-76.

[29] S. Rostami and F. Neri, A fast hypervolume driven selection mechanism for many-objective optimisation problems, Swarm Evol. Comput. 34 (2017) 50-67.

[30] E. Aggestam and J. C. O. Nielsen, Multi-objective optimisation of transition zones between slab track and ballasted track using a genetic algorithm, J. Sound Vib. 446 (2019) 91-112.

[31] X. S. Yang and S. Deb, Multiobjective cuckoo search for design optimization, Comput. Oper. Res. 40 (6) (2013) 1616-1624.

[32] C. A. X. da Silva, E. Taketa, E. H. Koroishi, F. A. Lara-Molina, A. W. Faria and F. S. Lobato, Determining the parameters of active modal control in a composite beam using multi-objective optimization flower pollination, J. Vib. Eng. Technol. 8 (2) (2020) 307-317.

[33] T. L. Saaty, A scaling method for priorities in hierarchical structures, J. Math. Psychol. 15 (3) (1977) 234-281.

Author information

Yuanfeng Wu received the M.S. degree from Hefei University of Technology (HFUT), Hefei, China, in 2021. He is a Ph.D. student in the School of Mechanical Engineering of HFUT. His current research interests include vibrations and waves in the continuous mechanical system, nonlinear dynamics, and intelligent optimization theory.

Enwei Chen received his Ph.D. from HFUT, Hefei, China, in 2006. Presently he is a Professor at School of Mechanical Engineering, HFUT. His current research interests include: noise and vibration control; parametric vibrations of structural system.

Neil Ferguson received his Ph.D. from the Institute of Sound and Vibration Research (ISVR), University of Southampton, UK in 1988. He has worked extensively on structural dynamics modeling, vibroacoustics and control. He is a senior lecturer at ISVR where he has been since 1986.

Yuteng He is a Ph.D student in the School of Mechanical Engineering of HFUT. He mainly researches the vibration of an axially moving string system, traveling wave method, vibration suppression, etc.

Haozheng Wei received his Ph.D. from HFUT, Hefei, China, in 2010. He is an associate scholar at School of Mechanical Engineering, HFUT.

Yimin Lu is an associate professor at School of Mechanical Engineering, HFUT. His current research interests include: noise signal detection and processing, and vibrations in the continuous mechanical system.